## Slide 1: Way Forward on V2X RRM requirement
LG Electronics, CATT
3GPP TSG-RAN WG4 Meeting #81 R4-1610693
Reno, Nevada, USA, 14 - 18 Nov, 2016
Agenda Item: 8.20.4

## Slide 2: V-UE UE Tx timing requirement
  NTA offset
  Requirement for eNB & GNSS as time reference:
    follow TS36.211
      NTA offset = 624Ts for IC conditions and operation on a shared UL/V2V carrier in TDD mode
      NTA offset = 0Ts for all other cases
  Requirement for SyncRef UE as time reference
    UE OoC & SyncRef UE OoC: NTA offset = 0Ts
    Other cases : FFS
  FFS : above agreements need to be revised based on the further study of NTAoffset
  Timing accuracy requirements for SyncRef UE as time reference
  Timing error(TE) requirement can be specified as ±[24] Ts

## Slide 3: P-UE UE Tx timing requirement
  GNSS as synchronization source
    Reuse the same transmit timing requirements (NTAoffset and TE) as for V-UEs
  eNB as synchronization source
    Reuse the same transmit timing requirements (NTAoffset and TE) as for V-UEs
  SyncRef UE as synchronization source: FFS

## Slide 4: Synchronization related requirements
  Open issues for further discussion (FFS if requirements should be introduced)
  GNSS synchronization source reselection evaluation period to prevent fast changes to/from GNSS synchronization source (ping pong effect)
    Companies encouraged to bring inputs on whether requirements need to be specified and duration of evaluation periods
      Tevaluate,GNSS,unreliable: minimum time before changing the synchronization reference from GNSS to another synchronization source
      Tevaluate,GNSS,reliable: minimum time before changing the synchronization reference from a synchronization source to GNSS
  V2V operation interruption due to synchronization source change to/from GNSS
    Motivation: During the synchronization source reselection UE changes timing and frequency reference which may result in TX/RX failure
    Companies encouraged to bring inputs on whether requirements need to be specified and duration of interruption period (e.g. 1 subframe)
  Selection time for GNSS as synchronization source
  UE behavior to maintain valid GNSS assistance information for GNSS as synchronization source
  WAN/GNSS timing misalignment
  Conditions for GNSS Reliability Requirements

## Slide 5: Interruption
Background: RAN1 definition of cases
  Case 1: UL TX and SL TX use separate TX chains and separate power budget
  Case 2: UL TX and SL TX use separate TX chains but sharing power budget
  Case 3: UL TX and SL TX share TX chains and power budget
V-UE interruptions requirement WAN and PC5 MCC operation
    Case 1: No interruptions
    Case 2: FFS
    Case 3: Interruptions may happen
    Interruptions may happen when SL has higher priority than UL. Priority definition is FFS.
  WAN and PC5 shared carrier operation
    There is interruption when SL has higher priority than UL
FFS on whether to capture interruption requirements in RAN4 specs

## Slide 6: Initiation/cease of SLSS requirements
eNB as time reference:
  Rel-12/13 in-coverage ProSe requirements on evaluation period can be reused for V2X.
GNSS as time reference:
  For out-of-coverage:
    Do not define any requirement.
  For in-coverage:
    Rel-12/13 in-coverage ProSe requirements on evaluation period can be reused
SyncRef UE as time reference:
  Accuracy requirement:
    Reuse D2D measurement accuracy requirements for V2V S-RSRP measurement accuracy.
  L1 measurement period/Evaluation Period for V2V S-RSRP (for 160ms PBCH period)
    320 ms : measurement period
    FFS : Evaluation Period

## Slide 7: SLSS detection requirement
Detection time of SyncRef UE
  FFS
Side condition
  FFS
V2V TX drop rate for SLSS monitoring and conditions
  when GNSS is used as time reference and the highest priority
    The V2X UE is not allowed to drop any SL V2X transmissions for the purpose of SLSS detection of other SyncRef UEs
  Other case
    FFS
UE measurement capability
  FFS

## Slide 8: Cell detection requirements in OOC
No cell identification requirement is defined for the V2X dedicated V2X carriers (i.e. carriers in Band 47 in Rel-14).
For carrier other than band47, the OoC cell detection requirements for V-UE are defined as 800ms

## Slide 9: Autonomous Resource (re)selection
Method to specify the requirement
  FFS
PSSCH-RSRP measurement accuracy
  Absolute accuracy: ± [5] dB
  Relative accuracy: ± [2.5] dB
  FFS : side condition
S-RSSI measurement accuracy
  FFS

## Slide 10: Congestion control
CBR requirement
  FFS