## Slide 1
3GPP TSG-RAN WG4 #82 R4-1700700 Athens, Greece, 13 - 17 February, 2017
Agenda item: 10.2 - Spectrum [FS_NR_newRAT]
Document for: Approval
Example LTE bands for NSA operation
KDDI Corporation

## Slide 2: Background
In RAN4-NR#1, which was held in January 2017, NR spectrum had been discussed.
Especially in [1], way forward on UE power sharing between LTE and NR was approved.
[1] R4-1700296 “WF on NSA operation between sub-6GHz and mmWave bands”, NTT docomo
In order to further study NSA operation (LTE-NR interworking), working assumption should be set.
Observation#1: Working assumption should be set in order to further discuss NSA operation.

## Slide 3: Discussion
    According to agreement in [1], spectra in mmWave (> 24 GHz) is assumed for NR and sub-6GHz bands are for LTE.
    RAN4 can also find operators’ preference in [2]. [2] R4-1700305 “WF on NR spectra related work”, NTT docomo <Results> Noted
    According to the list, we can find LTE bands as follows;  Bands 1, 3, 5, 7, 8, 20, 28, 40, 41, 42, 43
Observation#2: So far, Bands 1, 3, 5, 7, 8, 20, 28, 40, 41, 42 and 43 have been input as operators’ preference.
NOTE: This information was collected as NR spectra not for NSA operation.

## Slide 4: Discussion
    When RAN4 selects example bands for NSA operation, the list in [2] can be baseline.
    However, the list includes eleven bands. Therefore, it would be tough work for RAN4 to standardize all NSA specifications based on the list.
Observation#3: The list in [2] should be baseline but it would be tough work for RAN4 to standardize all.

## Slide 5: Discussion
    On the other hand, we guess some operators could not input their preference in January Adhoc due to issues on confidential, political, uncertain or something like that.
    Therefore, RAN4 may need more input from companies in order to complete list for NSA operation.
Observation#4: RAN4 may need more input from companies to complete list for NSA operation.

## Slide 6: Summary
    Current list in [2] includes eleven bands.  The number should be reduced.
    Current list may not reflect all of preference from RAN4.  More information should be collected.

## Slide 7: Proposal (= KDDI’s preference)
    We propose Bands 1, 26, 28, and 41 as example bands for NSA specification.
      This means that Band 26 is proposed to add into the list.
    We also propose selection policy as follows;
      The list in [2] should be baseline of LTE example bands for NSA specification’s work.
      Global bands should be prioritized, i.e., regional bands like Band 9 should be deprioritized.