## Slide 1
3GPP TSG-RAN WG4 #82 R4-1700712 Athens, Greece, 13 - 17 February, 2017
Agenda item: 7.22.1 - General [LTE_feMTC-Core]
Document for: Approval
Band 5 operation in Japan for FeMTC UE
KDDI Corporation

## Slide 2: Proposal
In [1], example bands for FeMTC were approved.
[1] R4-1610830 “WF on frequency bands for FeMTC”, KDDI, CHTTL
In [2] and [3], requirements on Band 5 operation in Japan were introduced only for UE category M1/NB1.
[2] R4-1610850 “Missing requirements for eMTC/NB IoT UE”, KDDI
[3] R4-1610497 “Missing requirements for eMTC/NB IoT UE”, KDDI
Proposal: For FeMTC Band 5 UE, requirements for Band 5 operation in Japan should also apply.

## Slide 3: How to introduce our proposal
    NOTE39 in Table 6.6.3.2-1 applies for FeMTC Band 5 UE.
    It seems that RAN2 will introduce new UE category, namely [Cat.M2] within this WI.
E-UTRA Band | Protected Band | Frequency Range (MHz) |  |  | Level (dBm) | MBW (dBm) | NOTE
5 | E-UTRA Band 1, 2, 3, 4, 5, 7, 8, 10, 12, 13, 14, 17, 23, 24, 25, 28, 29, 30, 31, 34, 38, 40, 42, 43, 45, 65, 66 | FDL_low | - | FDL_high | -50 | 1 | 
 | E-UTRA Band 26 | 859 | - | 869 | -27 | 1 | 
 | E-UTRA Band 41 | FDL_low | - | FDL_high | -50 | 1 | 2
 | FreE-UTRA Band 18, 19 | FDL_low | - | FDL_high | -40 | 1 | 39
 | Frequency range | 1884.5 | - | 1915.7 | -41 | 0.3 | 8, 39
 | Frequency range | FDL_low | - | FDL_high | -50 | 1 | 39
NOTE38: Applicable only for UE category M1 ,[M2] and NB1. |  |  |  |  |  |  | 

## Slide 4: Technical Justification
    NS_08 for Band 19 was specified by assuming Band 5 duplexer.
    For NRB > 44, 3dB A-MPR is required to protect Band 18/19 DL below -40 dBm/MHz.
    Maximum transmission bandwidth configuration for FeMTC feature is 25. This is much lower than NRB > 44.
    Therefore, even if the worst case is considered, FeMTC Band 5 UE can satisfy Japanese protection requirements.