## Slide 1
3GPP TSG-RAN WG4 #82 R4-1700714 Athens, Greece, 13 - 17 February, 2017
Agenda item: 7.23.1 [LTE_UE_cat_1RX]
Document for: Approval
B18 addition into Single Rx UE cat.1 WI
KDDI Corporation

## Slide 2: Background
In [1], frequency bands for single Rx category 1 were approved.
[1] R4-1610822 “Initial bands for single Rx category 1”, Qualcomm
In addition to the above, how to relax REFSENS requirements from 2Rx was also approved in [2].
[2] R4-1610187 “Single Rx Cat 1 reference sensitivity”, Qualcomm
Remaining work in RAN4 seems to be CR agreement for TS36.101.

## Slide 3: Proposal
    We propose to add Band 18 as initial bands for this WI.
    If this proposal is approved, initial bands for this WI is as follows;
      Bands 1, 2, 3, 4, 5, 7, 8, 12, 13, 20, 26, 39, 41 and 66.

## Slide 4: Analysis - Work road impact perspective -
    Impacted requirements due to this WI seems to be UE REFSENS.
      This means that how to decide relaxation value is only work load impacted factor.
    We believe that Band 18 REFSENS relaxation should be also 2.5 dB just same as approved way in [2].
      Therefore, if there is no objection to apply 2.5 dB relation on Band 18, no work load impact will be observed.