## Slide 1: WF on V2X RRM requirement
LG Electronics, CATT
3GPP TSG-RAN WG4 Meeting #82 R4-1700853
Athens, Greece, 13 - 17 Feb, 2017
Agenda Item: 7.20.4

## Slide 2: UE Tx timing requirement
  The scenario of shared carrier for WAN and PC5 V2X is not considered for RRM requirements in the current WI, assuming RF session will not define requirements for it.
  For V2X on Band 47 carrier, NTA offset should be always zero.
  Send a clarification to RAN1 to inform about RAN4 agreement and scenario that prioritized in RAN4.

## Slide 3: Interruption
V-UE requirement on WAN interruptions
  Case 2: Not capture this requirement
  Case 3: FFS
    Do not define if Case 3 is not supported in RF room
  WAN/GNSS timing misalignment
  Do not define
  V2X (re)configuration
  Specify 1 subframe WAN interruptions due to V2X (re)configuration

## Slide 4: Interruption
  Synchronous source change
  UE is allowed to drop V2V SL TX/RX for up to [1] subframe for every synchronization source change
  V2V/V2X interruptions due to WAN operation
  Do not define interruptions in Rel-14. Keep up to UE implementation.

## Slide 5: Initiation/cease of SLSS requirements
When timing reference is eNB/GNSS
  Reuse Rel-12/13 in-coverage ProSe requirements when UE is in-coverage
When timing reference is SyncRef UE
  Reuse D2D measurement accuracy
  Measurement period = 320ms
  Evaluation period = 640ms

## Slide 6: Selection/Reselection of V2X Sync.Ref.
Selection/Reselection to SyncRef UE
  GNSS is highest priority
    UE is synchronized to GNSS directly
      No SLSS and data drop allowed
    UE is Synced to SyncRefUE that is directly or in-directly synced to GNSS
      Not allow drop Data
      Need SLSS drop
        Side condition = [0] dB
        Tdetect,SyncRef UE = [1.6]seconds
        Allow to drop maximum [30]% of its transmission during Tdetect,SyncRef UE
          [3]samples based
    Other case
      Allow drop Data & SLSS
      Side condition = [0] dB
      Tdetect,SyncRef UE = [8]seconds
      Allow to drop maximum [6]% of its transmission during Tdetect,SyncRef UE

## Slide 7: Selection/Reselection of V2X Sync.Ref.
Selection/Reselection to SyncRef UE
  eNB is configured with the highest priority
    Allow drop Data & SLSS
    Side condition = [0] dB
    Tdetect,SyncRef UE = [8]seconds
    Allow to drop maximum [6]% of its transmission during Tdetect,SyncRef UE
  Decision are TBC based on RAN1 agreements in Feb meeting
UE measurement capability of performing S-RSRP
  V-UE : [3] identified SLSS
  P-UE : No SLSS related requirement is defined

## Slide 8: Selection/Reselection of V2X Sync.Ref.
  GNSS synchronization source reselection evaluation period
  Define evaluation period for synch source reselection from GNSS to another synch source. Value is TBD.
    Add a note that value will be finalize in Performance part or as maintenance

## Slide 9: Cell detection requirements in OOC
Not define due to there is no cell on carrier of V2X sidelink communication in Rel-14

## Slide 10: Autonomous Resource (re)selection
Only define the PSSCH-RSRP and S-RSSI measurement accuracy requirements for UE autonomous resource selection/reselection
PSSCH-RSRP measurement accuracy is specified for only absolute measurement.
  Absolute accuracy: ± [5] dB at Es/Iot [0]dB
  S-RSSI measurement accuracy
  Reuse RSSI measurement accuracy in LAA
  Measurement period
    Option1: Single-shot measurement requirements.
    Option2: filtered measurement requirements & measurement period= 1second
      Reuse the table from eLAA absolute RSSI measurement accuracy for S-RSSI relative accuracy
    Define both single shot and filtered with same accuracy.

## Slide 11: Congestion control
For CBR measurement, single-shot measurement requirements of S-RSSI shall be defined.