## Slide 1: Way forward on MPDCCH monitoring based requirements for feMTC
Nokia, Alcatel-Lucent Shanghai Bell, …
3GPP TSG-RAN WG4 Meeting #82
Athens, Greece, 13 - 17 February, 2017
Agenda: 7.22.3.2.1
R4-1700921

## Slide 2: Background
feMTC UE may be configured to monitor MPDCCH in a discontinuous manner.
Rel-13 eMTC UE RRM/RLM requirements are defined without considering MPDCCH monitoring configuration.
  UE power consumption may be impacted if it is required to activate its RF only for measurement purpose.

## Slide 3: WF
For feMTC, RLM and RRM requirements for connected mode are updated to take UE MPDCCH monitoring into account.
If UE is in non-DRX state, current non-DRX requirement is re-used unless the following conditions are met
  G is larger than 1, R_max*G is larger than MGRP, and
  UE is not configured with DRX, and
  UE does not detect it is scheduled in the MPDCCH monitoring period.
  in which case RLM/RRM requirements are scaled with r_max*G.
If UE is in non-DRX state, current non-DRX requirement is updated by replacing DRX cycle with max{DRX cycle, MPDCCH monitoring period}.
Interested companies should provide CR in RAN4#82bis.