## Slide 1: WF: MSD requirements for 2UL Inter-band CA combinations
LG Electronics
R4-1701199
3GPP TSG-RAN WG4 Meeting #82
Athens, Greece, 13-17 February, 2017

## Slide 2: Background [1]
Agreement on how 2UL Inter-band CA MSD requirements due to intermodulation exists [1]
  In short, only the worst case MSD is defined for each band
    This means that even if there are multiple IMD’s only the one resulting highest MSD is specified
  This agreement reflected to specify the MSD requirements for each CA band combos from Rel-12 and Rel-13.
One additional WF[2] was agreed in Rel-14 for 2UL inter-band CA which have multiple IMD’s for one band.

## Slide 3: Background [2]
For B3+B42 2UL CA MSD, MSD’s are analyzed as 29.8dB for IMD2, 8.0dB for IMD4, and 0.2dB for IMD5.
For xDL/2UL CA, some CA combos were multiple IMD impacts as below tables.
Currently, multiple MSD requirements in TS36.101 are defined , however it is quite burden to define test configuration for multiple MSD according to IMD orders and it will be more exhausted test time for all MSD tests.
Downlink CA configuration | Uplink CA Configuration | Harmonic relation to 3rd band without uplink | intermodulation to 3rd band without uplink | interference due to small frequency separation | MSD
CA_3A-7A-8A | CA_3A-7A |  | 3rd order | - | TBD
 | CA_3A-8A | B8 3rd harmonic | 2nd & 3rd order | - | Table 7.3.1A-0a for CA_3A-7A-8A [TS36.101], TBD for 2nd IMD TBD for 3rd IMD
CA_3A-5A-7A | CA_3A-5A | - | 2nd & 3rd order | - | [30.0] for 2nd IMD [18.0] for 3rd IMD
 | CA_3A-7A | - | 3rd order | - | [19.0]
 | CA_5A-7A | - | - | - | N/A

## Slide 4: Way forward
Proposal1: Basic principle should be follow the agreed WF [1]. For each UL Inter-band CA only the highest MSD is specified automatically in TS36.101.
Proposal2: Multiple IMDs for each CA band combos will be studied and analyzed in technical report.
Proposal3: From the defined multiple MSD requirements in TS36.101, only highest MSD requirements shall be maintained, the other will be moved into the related TRs.

## Slide 5: Reference
[1] R4-144031, “WF on 2UL inter-band CA MSD test configurations”, Mediatek, RAN4#71
[2] R4-164839, “WF: MSD definition for 2UL Inter-band CA combinations that have multiple IMD’s for one band”, Huawei, Hisilicon, RAN4 #79
[3] TR36.714-02-02
[4] TR36.714-00-02