## Slide 1: R4-1701898 Motivation for new WI on LTE DL 8Rx antenna ports Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting #82
Athens, Greece, February 13- 17, 2017
Document for: Information
Agenda Item: 12

## Slide 2: Motivation
  Recently clear market needs are observed
  Boost downlink peak data rate to 1.2Gbps and 1.6Gbps by using 8-layer transmission.
  New UE DL category 18 and 19 were introduced correspondingly.
    RAN4 should specify new RF, RRM and demodulation performance requirements.
  Benefits：
  Higher peak data rate and higher spectrum efficiency are available.
  Improve the downlink throughput.
  Improve the coverage.
  Make high order modulation like 256QAM and 1024QAM usable in more practical operating SINR range.
  Be capable of canceling more inter-cell interferences.

## Slide 3: Objectives
  Core requirements
  Specify RF core requirement such as REFSENS.
  Specify RRM core requirement such as RLM.
  Performance requirements
  Specify the channel model including correlation matrices for 8Rx antennnas
  Specify corresponding RRM tests such as RLM and application rules
  Specify demodulation performance, CSI reporting requirements, and application rules
    Identify a minimum set of necessary requirements for PDSCH, PDCCH/PCFICH, PHICH, PBCH, EPDCCH to achieve a good trade-off between test coverage and test case number.
    Assume MMSE and MMSE-IRC as baseline receivers
    Specify methodology including antenna connection to reuse the existing demodulation performance requirements, which are not covered by the minimum set of requirements.
    Use the methodology to specify 4Rx requirements as starting point.
  Both core and performance requirements will cover the single carrier and CA scenarios