## Slide 1: Way forward on phase noise model for NR
Agenda Item: 10.1.1.1
Document for: Approval
Source: Nokia
3GPP TSG-RAN WG4 meeting #82 Tdoc R4-1702035
Athens, Greece, 13 - 17 February, 2017

## Slide 2: Background
5 contributions discussed in agenda item 10.1.1.1
  R4-1700591 On EVM with different subcarrier spacing in the presence of phase noise, Intel
  R4-1700725 Phase noise model for NR, Nokia, Alcatel-Lucent Shanghai Bell
  R4-1701315 Phase noise model for above 6GHz, Huawei, Hisilicon
  R4-1701165 On mm-wave phase noise modelling, Ericsson
  R4-1701164 TP for 38.803: mm-wave phase noise and phase noise model, Ericsson
These contributions contain parameterized models. In some cases, parameters are estimated and in others, checked by measurement of prototype hardware.
Comparing the models, two issues standing out in particular are the assumption on PLL bandwidth (whether ~1MHz or significantly smaller) and the PN floor at high offsets.
  Other differences may be identified on closer analysis
This contribution summaries the issues and agreed WF for phase noise model

## Slide 3: Way forward
Define an oscillator phase noise model and related parameter configurations for simulation purposes
Model total oscillator PSD by using a PLL-based model in the phase domain including the impact of reference clock, loop filter noise and VCO sub-components
Include a description of the impact of feasible component FOM, frequency, power consumption, loop bandwidth and PN floor at high offset to the oscillator PSD model and/or to its parameterization(s)
  Propose a range for each of the respective parameters
  Provide justification for the proposed values/range for these parameters
    In particular for PLL bandwidth describe whether a BW of around 1MHz is achievable or why not
  Consider alternative approach based on measurements to verify the presented model
Define the dependency of the oscillator PSD level w.r.t carrier frequency of the oscillator output