## Slide 1: WF on noise floor rise of ICS and dynamic range requirement
ZTE, CATT, Nokia, NTT DoCoMo,Huawei,[Samsung,NEC,CMCC,China Unicom]
3GPP TSG-RAN WG4#82 meeting
Athens, Greece, 13 - 17 Feb, 2017
R4-1702040
Agenda item: 10.4.3.3
Document for: Approval

## Slide 2: Background
For dynamic range requirement of E-UTRA BS, power level of wanted signal and interfering signal is specified as following :
PIntf = -174+10*log10(BWchannel) + NF + 20
Pwanted= = -174+10*log10(BWwanted) + NF + 20+SNR+IM
Where 20dB noise floor rise is derived according to the system level simulation.
For ICS requirement of E-UTRA Bs, power level for wanted signal and interfering signal is specified as following:
PIntf = -174+10*log10(BWIntf) + NF + SNR+IM+16
Pwanted= = -174+10*log10(BWwanted) + NF +SNR+IM
Where 16dB noise floor rise is also derived according to system level simulation.
In addition, as channel bandwidth, noise figure and physical layer channel is still under discussion, therefore only noise floor rise could be investigated according to current status.
[1] R4-1701451, Discussion on receiver dynamic range of NR BS,ZTE
[2] R4-1701453, Discussion on receiver ICS requirement of NR BS,ZTE

## Slide 3: Way forward
To Investigate the noise floor rise for dynamic range and ICS requirement for NR BS firstly in RAN4;
For above 24GHz:
reuse the existing simulation assumptions of WP5D coexistence study captured in the TR 38.803 for preliminary study;
Other options are not precluded in the future.

## Slide 4: Work plan
RAN4#82bis
to align the initial simulation results among the interested companies;
RAN4#83 ~RAN4#84
to make the final agreement for this perspective with updated simulation assumption;