## Slide 1: WF on NR BS receiver requirement
ZTE,CATT, NTT DoCoMo,[Nokia, Huawei, Ericsson,Samsung]
3GPP TSG-RAN WG4#82 meeting
Athens, Greece, 13 - 17 Feb, 2017
R4-1702041
Agenda item: 10.4.3.3
Document for: Approval

## Slide 2
Information
NR BS receiver requirement | Contribution
REFSENS | R4-1700862,NR BS conduct sensitivity granularity, ZTE
Dynamic range | R4-1701451,Discussion on receiver dynamic range of NR BS,ZTE
In channel selectivity | R4-1702034, WF on in-band requirements for multiple numerologies for NR, Nokia R4-1701453, Discussion on receiver ICS requirement of NR BS,ZTE
ACS&NBB | R4-1701454,Discussion on ACS and Narrowband Blocking requirement of NR BS, ZTE
Blocking | R4-1701672, Proposals on further simulation assumptions for NR BS blocking, Nokia R4-1701455, Discussion on blocking requirement for NR BS, ZTE
Intermodulation | R4-1701457,Discussion on receiver intermodulation requirement of NR BS,ZTE
Spurious emission | No contribution

## Slide 3: Background: Blocking
For in-band blocking of E-UTRA BS, power level of interfering signal is derived according to the system level simulation in [1]. Based on the current SI status, only the power level of interfering signal was could be further investigated .
For out of band blocking of E-UTRA BS, Out-of-band blocking level of –15dBm is proposed based on analysis presented in Tdoc R4-99038 in Turin, however this -15dBm in R4-99038 is for out of band blocking at UE side , therefore it ‘s necessary to check the rational for NR BS instead of reusing directly.
[1] R4-1701455, Discussion on blocking requirement of NR BS,ZTE
[2] R4-1701672, Proposals on further simulation assumptions for NR BS blocking, Nokia, Alcatel-Lucent Shanghai Bell

## Slide 4: Way forward :Blocking
To Investigate power level interfering signal of in-band blocking by system-level simulation in RAN4;
For above 24GHz:
Derive a methodology for deriving a OTA interferer and wanted signal level rather than a conducted interferer level
If possible reuse the existing simulation assumptions of WP5D coexistence study captured in the TR 38.803 with slight modification for preliminary study;
Other options are not precluded in the future.
Statistical method:
Discuss and agree on what blocker and wanted signal probabilities to use in the simulations
For below 6GHz:
whether reusing the same scenarios and cryteria as used in exiting E-UTRA requirements (37.104/37.105) should be further discussed in the next meeting.
To further check the interfering signal power level of out of band blocking instead of reusing directly as E-UTRA BS for both above 24GHz and below 6GHz.

## Slide 5: Background: intermodulation
For general intermodulation requirement and narrow band intermodulation requirement of E-UTRA BS, power level of interfering signals could potentially beare derived according to the system level simulation in [1].
Whether any other approaches than system simulations are needed should be discussed further
[1] R4-1701457, Discussion on receiver intermodulation requirement of NR BS,ZTE

## Slide 6: Work plan
RAN4#82bis
Agree OTA criteria and statistical method to be used for the simulation
to align the initial simulation results from interested companies;
RAN4#83-RAN4#84
to make the final agreement for this perspective with updated simulation assumption;