## Slide 1: WF on NB-IoT: NB intermodulation and spurious response issue
Ericsson
3GPP TSG-RAN WG4 Meeting #82
Athens, Greece, 13-17 Nov, 2017
Agenda Item: 5.5.3
R4-1702055

## Slide 2: Background
A potential spur issue was raised in R4-1700833 regarding NB-IoT and narrowband intermodulation requirement.
  Origin of the spur issue has been further explained via email (copied in Annex).
Depending on radio design, spur might exist or not.
When it happens, spur could hit a NB-IoT tone and impact radio performance: radio would not pass NB intermodulation test, while NB IM3 interferer exists at that power level (which is actually the goal of this requirement).
More analysis on the issue is required in the discussion.

## Slide 3: Way Forward
For next RAN4#82b meeting, companies are encouraged to:
  Get good understanding of potential spur issue (R4-1700833 + Annex) and impact evaluation.
  Assess whether the spur issue has to be addressed
  Further analyze which solution to overcome this issue (if confirmed) should be applied:
    Reduce CW and LTE PRB power level
    Shift CW frequency by X kHz and LTE PRB by 2*X kHz (Nokia’s suggestion).
    Move CW signal on the other side of LTE PRB (Ericsson’s proposal – R4-1700833. Note that CW and LTE PRB power level should only be increased by 1dB, not 3dB as written in proposal).
    any other alternative is not precluded.

## Slide 4: Way Forward
During RAN4#82b meeting:
  Conclude whether this spur issue should be addressed.
  If so, select the best option to address it.

## Slide 5: Annex – email Feb. 11th 2017 (1/3)
In the following, I’m so starting with some basics (to make sure we’re aligned) and further discussed issue’s impact.
The structure for a generic (simplified) receiver looks like this:
All signals present at the antenna that pass the bandpass filter is frequency converted in the mixer.
In the above simplified receiver the output will be:
The problem with the above is that it assumes that the LO is ideal.

## Slide 6: Annex (2/3)
But any real LO has phase noise and in some cases spurs, that’s depending on radio design. Here is a snapshot of an “old” synthetizer.
If a spur exists or not, its position and amplitude, depends on the design of the LO, e.g. old integer-PLL synthesizers have spurs, leakages on the circuit board could cause spurs, …
When the LO is not ideal, the output is reciprocal mixing of the input signal and LO.
This means that the output of the CW-signal will look like this
While the modulated signal will look like this:

## Slide 7: Annex (3/3)
For the modulated signal, each signal component is mixed with the LO so the output at each frequency is the sum of the contributions from all mixer products.
This means that the spur is not a spur anymore as it is modulated with the modulated signal.
As a result of this, the spur level is not a problem anymore as the energy is spread out over a bandwidth.
But a CW-signal close to a wanted LTE-signal will affect the performance.
Here, the green rectangle represents a wanted LTE-signal.
The phase noise might (slightly) affect the sub-carrier(s) at the edge of the LTE-signal.
But if the spur hits a NB-IoT sub-carrier, impact is not neglictable anymore.
Again, for LTE, this is not an issue as we consider the full (green) BW, but for NB-IoT it is as it’s only one sub-carrier.