## Slide 1: 3GPP TSG-RAN WG4 Meeting #82 Athens, Greece, 13 - 17 February 2017
Huawei, Ericsson, Nokia, Alcatel-Lucent Shanghai Bell
Way forward on eLAA demodulation performance
R4-1702146

## Slide 2: Background
As per the agreed WID RP-161832, the eLAA core part is complete and corresponding possible UE and BS demodulation performance requirements need to be defined.

## Slide 3: UE demodulation performance
No new UE demodulation performance test needs to be defined

## Slide 4: BS demodulation performance requirements

## Slide 5: General
New PUSCH demodulation performance requirements need to defined for eLAA:
Test Purpose:
  Verify PUSCH new interlace resource structure
  FFS: Verify DM-RS channel estimation performance with contiguous interlace allocation
  FFS: Verify PUSCH demodulation performance with UL LBT model
  In Rel-14, one PCell with 20MHz + one LAA Scell with UL and 20MHz BW will be defined.
  Number of UE to be modeled
    Single UE
  Test applicability for future possible multiple licensed bands + multiple unlicensed bands will be discussed later.

## Slide 6: General
Starting PUSCH symbol configuration
  ‘01’ (25µs in symbol 0);
Ending symbol configuration
  Option 1: Up to OFDM symbol 13
  Option 2: Up to OFDM symbol 12
UL grant Scheduling
  One stage scheduling
Reference receiver:
  MRC

## Slide 7: General
Resource allocation
  Contiguous interlace allocation
    One or more interlace allocation is TBD
  Investigate the channel estimation for different number of contiguous interlace allocation
LAA Sell Carrier Scheduling
  Self-carrier scheduling for both UL and DL
Antenna configuration
  Tx: 1; RX: 2 and 4
Channel model
  Option 1: EPA5 Low,
  Option 2: EVA5 Low
Modulation
  QPSK 1/3 and 16QAM ¾ as baseline, 64QAM 5/6 is decided in next meeting
Test metric: 70% TP

## Slide 8: UL burst transmission model
UL burst transmission model needs to be defined
  Option 1: UL burst transmission is modelled
  Option 2: No UL burst transmission model
Companies can provide simulation for alignment with interlace resource allocation with no UL burst transmission model.