## Slide 1: 3GPP TSG-RAN WG4 Meeting #82 Athens, Greece, 13 - 17 February 2017
Huawei, China Telecom, Nokia, Alcatel-Lucent Shanghai Bell, ZTE
WF on BS IC Interferer number and Link level Simulation assumptions
R4-1702162

## Slide 2: Background
During RAN4#81 Reno meeting, WF of R4-1610707, R4-1610712, R4-1610711 and R4-1610661 for BS IC were approved, many agreements were reached.

## Slide 3: Inter-cell interferer number
Model 1 inter-cell interferer for 4Rx with high interference level

## Slide 4: Link level simulation assumptions -1
DMRS sequence for the intra-cell and inter-cell UEs
  The cell id for the intra-cell UEs is 0, and the cell id for inter-cell interfering UE is 1.
  Group hopping and sequence hopping are disabled, and = 0 for all the simulated PUSCHs.
  = {0, 6} for 2 intra-cell UEs, = {0, 3, 6, 9} for 4 intra-cell UEs ; and = 0.

## Slide 5: Link level simulation assumptions -2
Rx Antenna Number
  Focus on 2 and 4 Rx BS
  To capture the following text into the TR
    For 8Rx BS, on one hand, IC gain is relatively limited for up to 4 intra-cell UEs; on the other hand, a large number of channel faders are needed for potential 8Rx IC test. Thus this SI focuses on 2 and 4 Rx BS.
MCS level
  Companies are invited to provide results for MCS 10&15, and companies are also welcome to provide results for MCS 21.
Performance measurement
  Definition of SINR
    Intra-cell inter-user interference is not included in the “I” part of SINR, and SINR represents signal to inter-cell interference and noise ratio.
  Performance measurement point
    Take the SINR at 85% maximum throughput as the performance measurement point.