## Slide 1: WF on UL enhancement
CMCC, Nokia, Alcatel-Lucent Shanghai Bell, Ericsson
3GPP TSG-RAN WG4 Meeting #82 Athens, Greece, 13th - 17th February 2017
Agenda Item: 7.16.3
R4-1702302

## Slide 2: Simulation assumption for UL 256QAM
Parameters | Value
Maximum number of HARQ transmissions | 4
RV sequence | 0, 2, 3, 1, 0, 2, 3, 1
Uplink-downlink allocation for TDD | Configuration 1 (2:2)
Tx number | 1
Rx number | 2, 4, 8
CP type | Normal
Propagation conditions and antenna correlation | EPA 5Hz Low
PRB allocation | Full PRB
MCS | MCS26 or MCS 27
System Bandwidth | 1.4MHz, 3MHz, 5MHz, 10MHz, 15MHz, 20MHz
UE TX EVM | 0 or 3.5%, to be down selected next meeting, companies are encouraged to provide simulation or analysis
Channel estimation | Realistic
Performance metric | SNR at 70% Maximum throughput

## Slide 3: Test methodology for PUSCH in UpPTS
Option 1: only special subframe is scheduled in the test
  Simulation results for PUSCH in UpPTS to be provided
Option 2: both special subframe and normal UL subframes are scheduled in the test
  Simulation results for performance of PUSCH in UpPTS and normal UL subframes to be provided
  Simulation assumptions are provided in the next slide
Down selection of the test methodology in next meeting

## Slide 4: Simulation assumptions for PUSCH in UpPTS
Parameters | Values
TDD UL/DL configuration | 1
Special subframe configuration | 10
TTI bundling | Disabled
CP length | Normal
Number of data symbols | 5
DMRS | In symbol#3 in UpPTS
Number of TX antennas | 1
Number of RX antennas | 2, 4, 8
Antenna correlation | Low
System BW | 1.4MHz, 3MHz, 5MHz, 10MHz, 15MHz, 20MHz
PRB allocation | Full BW
MCS | 16QAM with 3/4 coding rate 64QAM with 5/6 coding rate
Propagation conditions | EPA5
Table 2 Simulation assumptions for PUSCH in UpPTS

## Slide 5: Way Forward
Companies are encouraged to provide simulation results based on the simulation assumption in the next meeting.