## Slide 1: WF on NR BS receiver requirement
ZTE,CATT,NEC
3GPP TSG-RAN WG4#82 meeting
Athens, Greece, 13 - 17 Feb, 2017
R4-1702352
Agenda item: 10.4.3.4
Document for: Approval

## Slide 2
Information
NR BS receiver requirement | Contribution
REFSENS | R4-1700862,NR BS conduct sensitivity granularity, ZTE
Dynamic range | R4-1701451,Discussion on receiver dynamic range of NR BS,ZTE
In channel selectivity | R4-1702034, WF on in-band requirements for multiple numerologies for NR, Nokia R4-1701453, Discussion on receiver ICS requirement of NR BS,ZTE
ACS&NBB | R4-1701454,Discussion on ACS and Narrowband Blocking requirement of NR BS, ZTE
Blocking | R4-1701672, Proposals on further simulation assumptions for NR BS blocking, Nokia R4-1701455, Discussion on blocking requirement for NR BS, ZTE
Intermodulation | R4-1701457,Discussion on receiver intermodulation requirement of NR BS,ZTE
Spurious emission | No contribution

## Slide 3: Background: Blocking
For in-band blocking of E-UTRA BS, power level of interfering signal is derived according to the system level simulation in [1]. Based on the current SI status, only the power level of interfering signal was further investigated .
For out of band blocking of E-UTRA BS, Out-of-band blocking level of –15dBm is proposed based on analysis presented in Tdoc R4-99038 in Turin, however this -15dBm in R4-99038 is for out of band blocking at UE side , therefore it ‘s necessary to check the rational for NR BS instead of reusing directly.
[1] R4-1701455, Discussion on blocking requirement of NR BS,ZTE
[2] R4-1701672, Proposals on further simulation assumptions for NR BS blocking, Nokia, Alcatel-Lucent Shanghai Bell

## Slide 4: Way forward :Blocking
To Investigate power level interfering signal of in-band blocking by system-level simulation in RAN4;
For above 24GHz:
Derive a methodology for deriving a OTA interferer and wanted signal level rather than a conducted interferer level
If possible reuse the existing simulation assumptions of WP5D coexistence study captured in the TR 38.803 with slight modification for preliminary study;
Other options are not precluded in the future.
Statistical method:
Discuss and agree on what blocker and wanted signal probabilities to use in the simulations
For below 6GHz:
to follow the eAAS discussion. revisit eAAS if inconclusive. Recheck status every RAN4 meeting.
To further check the interfering signal power level and frequency range of out of band blocking instead of reusing directly as E-UTRA BS for both above 24GHz and below 6GHz.
In the absence of guidance on frequency range for out of band blocking requirements for NR, to further check if the proposal to adopt the range from 30 MHz to 26GHz for frequency bands above 6 GHz up to 13GHz and 30MHz to 2nd harmonic for above 13 GHz bands is acceptable or to consider alternative proposal.
Narrrowband blocking in the in-band frequency range will be not specified for NR BS above 24GHz if there is no narrowband system (e.g. GSM )operation in that frequency range.

## Slide 5: Background: intermodulation
For general intermodulation requirement and narrow band intermodulation requirement of E-UTRA BS, power level of interfering signals could potentially be derived according to the system level simulation in [1].
Whether any other approaches than system simulations are needed should be discussed further.
Narrowband intermodulation in the in-band frequency range will be not specified for NR BS above 24GHz if there is no narrowband system (e.g. GSM ) operation in that frequency range.
[1] R4-1701457, Discussion on receiver intermodulation requirement of NR BS,ZTE

## Slide 6: Work plan
RAN4#82bis
Agree OTA criteria and statistical method to be used for the simulation
to align the initial simulation results from interested companies;
RAN4#83-RAN4#84
to make the final agreement for this perspective with updated simulation assumption;