## Slide 1: Way Forward on UE RF Requirements
Qualcomm Incorporated, Ericsson, Intel
3GPP TSG-RAN WG4 Meeting #82 R4-1702371
Athens, Greece, 13-17 February, 2017

## Slide 2: Antenna Configurations
Further study UE Rx and Tx path configuration for which requirements should be defined
For Rel-15 EMBB sub-6
  Baseline is 1 Tx 2 Rx
For mmWave, the following will be studied for high level architecture assumptions to be used for EIRP/EIS requirement and test study but these don’t limit the implementation
  Antenna polarization: Dual-polarization or single polarization
  Antenna number: Total number and/or number for each polarization
  BB path number: Total number and/or number for each polarization

## Slide 3: Spherical coverage Requirement
Chairman minutes for RAN4#82 captured the Agreement:
  Proposal: For CDF method, RAN4 method for describing spherical coverage of RF parameters is CDF where each point represent equal surface area in sphere surrounding the UE.
    Companies are encouraged to study the advantage of this CDF method.
    The other method(s) are not precluded.
Following aspect on defining spherical coverage requirements were agreed
  EIRP and EIS requirements can be defined based on a CDF
    CDF will be based on data taken in connected mode and by measuring EIRP and/or EIS after UE beamforming
    Link antenna position in relation to UE is changed for each testpoint
    Each test point represents an equal surface area on a sphere surrounding the UE The surface area corresponding to each test point is equal to all UE types with different spherical requirement
    Test point defintion, applicability of CDF-based requirements, method and quantity are FFS
  Other parameters are FFS
  Companies are encouraged to study the advantage of this CDF method.
  The other method(s) are not precluded.

## Slide 4: Tx Power Requirement
Minimum of peak EIRP
  Requirement of peak EIRP level should be studied, if peak EIRP is defined FFS.
  Proposed value range [27dBm-34dBm]
  How to define is FFS, min of peak, min of 90 % in CDF
Maximum allowed TRP
  It should be studied whether TRP should be limited by defining a maximum allowed TRP to limit co-channel interference
  Value is FFS
Power Class
  Power class should be defined based on maximum EIRPif peak, average, minimum EIRP will be used FFS
  Whether TRP is used for power class definition is FFS: unwanted emissions are specified as TRP and must be met by a device for any in-channel TRP up to its maximum power capability for the UE and (regardless of the antenna configuration)
Minimum Power
  Minimum power level is FFS regalrd

## Slide 5: Out of Band Blocking
Blockers for >24GHz should be studied based on the systems deployed in adjacent bands
Companies are encouraged to bring more information on deployed systems in all regions
Companies should share their current view on what are expected values/ at least the direction in which the frequency range definition & power level of blockers should progress further.
Studying every single radio system should be dealt with caution in favour of time availability.

## Slide 6: Out of Band Blocking
Previous contributions:
R4-1702043, Out of band blocking for UE receivers, Intel
R4-1700261, RF filters for mm-wave OOB blocking, Intel
R4-1609756, Out-of-band blockers in the mm-wave spectrum, Qualcomm
R4-1700097, Spurious emissions for mmWave, Qualcomm
R4-1702051/R4-1702052, Update on out-of-band blockers in the mm-wave spectrum(US/EU), Qualcomm
R4-1701504, UE blocking requirement consideration for mmWave, Huawei

## Slide 7: Reference architecture (10.4.2.1)
Background
  R4-1701333, On UE architecture assumptions, Huawei
  R4-1701449, 5G UE reference architecture, LG
  R4-1700604, UE reference architecture for mmWave, Intel
A high level of the architecture including impairments are given in these contributions.
The different impairments - which depend on the reference architecture - need to be further study, such as:
  PA nonlinearity
  IQ imbalance
  Phase noise
  EVM degradation
  Intermediate Frequency related issues for above 24GHz such as emissions and blocking behavior.