## Slide 1: WF on NB-IoT new power class
Nokia, Alcatel-Lucent Shanghai Bell,
R4-1702422

## Slide 2: Background information
REFERENCES
[1] R4-1701007 Necessary specification changes due to introduction of new UE Cat NB1 power class, Nokia
[2] R4-1701266 RF requirements for the new NB-IoT UE power class, Huawei, Neul
How to define new +14 dBm power class for NB-IoT has been discussed in RAN4#82 [1][2]. During the meeting RAN2 decided to introduce new UE category NB2 under NB-IoT enhancement WI. RAN2 agreements do not restrict the power class usage to NB2 only. Furthermore RAN2 has agreed that if NB-IoT UE supports cat NB2 it also supports cat NB1. NB-IoT UE can indicate only one power class. RAN2 has agreed NPRACH enhancements for rel-14 for new NB-IoT lower power class.
Introduce UE category NB2 for NB-IoT that indicates the support of larger TBS sizes of 2536 bits. A UE that supports NB2 shall also support NB1.
From RAN2#79 meeting minutes

## Slide 3: WF on NB-IoT new power class
Proposal 1: Power class 6 = + 14 dBm (±2.5) is applicaple to NB-IoT UE categories NB1 and NB2
Proposal 2: UE Cat NB1 PC 3 and PC 5 emission requirements (SEM, ACLR and spurious emissions) are applicaple also to NB-IoT PC 6 UE.
Proposal 3: No MPR is allowed for NB-IoT PC 6 UE
Proposal 4: PC 6 is release independent from release 14 owards.

## Slide 4: WF on NB-IoT new power class Pcmax tolerance
Proposal 5: NB-IoT PC 6 Pcmax tolerance is specified according to Table 1.
PCMAX,c (dBm) | Tolerance T(PCMAX,c) (dB)
13 ≤ PCMAX,c ≤ 14 | 2.5
12 ≤ PCMAX,c < 13 | 3.5
11 ≤ PCMAX,c < 12 | 4.0
8 ≤ PCMAX,c < 11 | 5.0
5 ≤ PCMAX,c < 8 | 6.0
-40 ≤ PCMAX,c < 5 | 7.0
Table 1: PCMAX tolerance for NB-IoT PC 6 UE power class 6