## Slide 1: WF on NR band structure
Huawei, HiSilicon, China Unicom, Telefonica, Deutsche Telekom, Orange, CMCC, China Telecom
3GPP TSG-RAN WG4 Meeting #82
Athens, Greece, 13 - 17 February, 2017
Agenda item: 10.2
Document for: Approval
R4-1702443

## Slide 2: Background
In RAN4 NR AH#1-2017, the following agreement was reached in R4-1700298
  The requirements for LTE-NR co-existence with uplink sharing should be specified in Rel-15 NR WI
    To specify the requirements, the frequency range of LTE bands where the UL carrier is shared by LTE and NR needs be introduced.
    Additionally, the pairing of UL in such band with DL NR band used should be defined.
    The candidate LTE bands will be discussed in the next meeting and the further discussion is needed to keep reasonable workload.
    The details on the requirements are FFS.
To facilitate such uplink sharing with SDL and TDD spectrum, a concept of “band package” is proposed in [R4-1701820].

## Slide 3: Way forward
If NR bands need to be defined in a new way compared to LTE and how to do it can be further studied to consider the following aspects. It is FFS how to carry out such study.
    Feasibility study should be conducted by considering
      Benefits compared to current band structure with practical assumptions and limitations
      Implementation impact and complexity of both BS and UE
    Regulatory aspects
    Specification impact and complexity
      Timeline with respect to other RAN4 R15 NR work
  The requirements for LTE-NR co-existence with uplink sharing should be specified in Rel-15 NR WI. If LTE-NR co-existence with uplink sharing will be included in the Rel-15 NR WI, RAN4 should study the possible band combinations according to operators’ interests, for example, Bands 20/28/8/1 (UL) + C band (UL/DL), by consideringBand 20/Band 28/Band 8/Band 1 (UL)+C-band (UL/DL)
    Whether 1UL or 2 ULs will be allowed should be studied further
    Impact on implementation such as flexible duplex distance, as well as specification complexity needs to be studied
    The exact completion date is FFS and set in such a way that progress on NSA is not impacted.