## Slide 1: WF: UE ON/OFF mask for sTTI
Qualcomm, Ericsson, ZTE, Nokia, Huawei
R4-1702507
3GPP TSG-RAN WG4 Meeting #82
Athens, Greece, 13-17 February, 2017

## Slide 2: Background 1
Mask for single sTTI
  ON to OFF mask is outside the sTTI duration
  OFF to ON mask is outside the sTTI duration
sTTI duration
t1 usec
t1 usec

## Slide 3: Background 2
ON/OFF mask for two consecutive sTTIs
  OFF to ON mask is outside the sTTI duration
  ON to OFF mask is outside the sTTI duration
sTTI duration
Transient period of ‘x’ usec
sTTI duration
t1 usec
t1 usec

## Slide 4: Way forward 1
Transient time (‘x’) for middle section
  Need to study the effect on demod for different values of ‘x’ (ex: 20 usec) on either side of the sTTI boundary
  If no frequency hopping or power change ‘x’=0
‘t1’ =[20] usec (legacy value)
  Other values will be investigated if there is proper justification
sTTI duration
Transient period of ‘x’ usec
sTTI duration
t1 usec
t1 usec

## Slide 5: Way forward 2
This is a case with no power change or frequency hopping between SRS and sTTI.
‘t1’ and ‘t2’ should correspond to the transient times of the corresponding times for sTTI and SRS respectively?
t1=[20] usec for example
t2=[20]usec for example
  Other values will be investigated if there is proper justification

## Slide 6: Way forward 3
In case of the middle transient ( in case of power change or freq hopping between SRS and sTTI)
  3 possible options:
    The transient time should be shared between SRS and DMRS or
    The transient time should be completely in DMRS and protect SRS as shown below.
    Or if the transient time to be in SRS ONLY and protect DMRS.
  What should be the value of the transient time between SRS and sTTI?

## Slide 7: Reference
R4-1701629, Further discussions on implication of ON/OFF mask on sTTI operations, Ericsson, 3GPP TSG-RAN WG4 Meeting #82
R4-1700449, On-OFF time mask for sTTI, 3GPP TSG-WG RAN4 Meeting #82
R4-1701257, Further discussion on UL ON/OFF time mask, 3GPP TSG-RAN WG4 Meeting #82