## Slide 1: WF for 4Rx CA 256QAM(1/2 layer) and 3/4 layers tests in Rel-14
Ericsson, AT&T, China Telecom, CMCC, NTT Docomo, SoftBank, Verizon, China Unicom, Sprint, Deutsche Telekom, Orange, T-Mobile USA, ZTE, Telecom Italia, Telia Company
3GPP TSG-RAN WG4 Meeting #82bis R4-1704207 Spokane, USA, 3rd-7th April, 2017
Agenda Item: 7.21.2.2
Document Type: Approval

## Slide 2: Background
256QAM(1/2 layers) tests are important deployment scenarios under CA to reach higher TP
Higher layers (3/4 layers) tests are also important deployment scenarios under CA to reach higher TP
Different CC has different propagation channel which may require different UE implementation properly to ensure both 256QAM(1/2 layers) and higher layers (3/4 layers) tests under CA deployment.

## Slide 3: Way forward
RAN4 agrees to specify the following performance test cases for Rel-14 4Rx CA WI
  256QAM(1/2 layers) tests
    The tests will be specified with single carrier requirement for both 2 Rx and 4Rx on multiple bandwidths on 5, 10, 15, 20MHz.
  Higher layers (3/4 layers) tests
    The tests will be specified with single carrier requirement for 4Rx on multiple bandwidths on 5, 10, 15, 20MHz.
The above tests will be specified with at least 2 CCs.

## Slide 4: Applicability rule for test coverage
For 256QAM CA tests once the CA tests are executed the corresponding single carrier tests can be skipped.
For 3 and 4 layer CA tests once the CA tests are executed the corresponding single carrier tests can be skipped.

## Slide 5: Test parameters
256QAM(1/2 layers) tests
  TM4 2 layers 4x4/4x2
  TM9 1 layer 2x4/2x2
Higher layers (3/4 layers) tests
  TM4 4 layers 4x4
  TM9 4 layers 4x4
The other test parameters are to be decided during email discussion after the meeting

## Slide 6: Applicability rule for rests
256QAM CA tests should follow the same applicability rule as IRC CA tests.
For 4 layers tests 2 steps to pick up the tests
  Select CA configurations with the maximum number of CCs supporting 4 layers MIMO among all supported CA configurations with any CA capability
  Select any one of the CA configuration with the largest aggregated CA bandwidth combinations on any 2CCs among all the CCs among all the selected CA configuration from Step 1