## Slide 1: WF on V2V demodulation tests
Huawei, HiSilicon, LGE, CATT
3GPP TSG-RAN WG4 Meeting #82bis R4-1704235
Spokane, USA, 3 - 7 April, 2017

## Slide 2: Background
V2V performance part is extended for two meetings, next meeting is the last meeting
During RAN4 #82 meeting, following agreements were reached:
  Single link performance
    For PSSCH, define following test cases
      EVA180, MCS13, 20MHz, retransmission: 0 time
      EVA2700, MCS4, 10MHz, retransmission: 1 time
    For PSCCH, define following test cases
      EVA1500
  Multi-link performance
  Introduce new power imbalance requirement
Some open issues need to be discussed

## Slide 3: Test metric
Test metric for PSSCH
  Option 1: 30% BLER
  Option 2: 10% BLER
Test metric for PSCCH
  1% BLER

## Slide 4: Test setup
TX signal time offset vs GNSS reference
  CP/2-12Ts

## Slide 5: Test scenarios
Single-link PSSCH test scenarios
  Consider small number of RB allocation for PSSCH
    Adjacent allocation(PSCCH-PSSCH)
      Candidates for requirements definition
        Option 1: 10 PRB
        Option 2: 5 PRB
      For investigation purposes: 20 PRB
  8 ms PSSCH retransmission delay

## Slide 6: Test scenarios
Multi-link fading test
  Do not define
GNSS assumption need to be specified according to RRM discussion

## Slide 7: Test scenarios
Power imbalance test
  Use non-adjacent RB allocation for 2UEs
  Use adjacent PSCCH/PSSCH for each UE
  ICS value
    Option 1: 30 dB
    Option 2: 25 dB
  Make decision on ICS value in next meeting

## Slide 8: Simulation assumption
PSSCH frequency offset estimation
  PSSCH DMRS
Channel estimation
  linear interpolation in time domain
  frequency domain MMSE equalization

## Slide 9: Specification structure
Specification structure
  14 Performance requirement (V2X sidelink communication)
    14.1 General
    14.2 Demodulation of PSSCH
    14.3 Demodulation of PSCCH
    14.4 Demodulation of PSBCH
    14.5 Power imbalance performance with two links
  More sections will be added for additional test cases