## Slide 1: WF for uplink in band blocking for the BS
R4-1704358
Ericsson

## Slide 2: WF for uplink in band blocking for the BS
Two possibilities for the blocking probability have been considered:
  99.99%, corresponding to 0.01% loss of TTIs due to blocking
  99%, corresponding to 1% loss of TTIs due to blocking
Justification why the probability and associated TTI loss selected is appropriate should be agreed, so that a consensus on whether to use 99% or 99.99% can be achieved.
To make a final decision on blocking, the OTA blocking level, desensitization and absolute OTA reference sensitivity will all need to be considered.

## Slide 3: WF for uplink in band blocking for the BS
For setting an OTA blocking requirement, methods to derive an OTA level need to be considered further, e.g. considering omnidirectional pattern, omnidirectional pattern based on the highest power UE as discussed in this meeting or other proposals.
The OTA blocking requirement should be checked that it is not over/under dimensioned for different deployment scenarios or BS architectures.