## Slide 1
3GPP TSG-RAN WG4 Meeting #84 R4-1708556
Berlin, Germany, 21 – 25 Aug 2017
Source: Keysight Technologies, Rohde & Schwarz, Anritsu, Spirent, Bluetest
Title: WF on channel modelling
Agenda item: 9.7.3.1
Document for: Approval

## Slide 2: Input documents
The following Tdocs were presented on channel modelling
[1] | R4-1707129 | Reduced complexity millimeter wave OTA channel models evaluation candidates | Azimuth Systems Incorporated
[2] | R4-1707130 | Metrics for comparing reduced complexity models for millimeter-wave OTA demodulator testing | Azimuth Systems Incorporated
[3] | R4-1707131 | Evaluation of reduced complexity millimeter wave OTA channel models for UE demod testing | Azimuth Systems Incorporated
[4] | R4-1707348 | Channel Modelling for RAN4 RRM and Demodulation Testing | Spirent Communications
[5] | R4-1708176 | Channel Model for OTA RRM/Demod Testing | Keysight Technologies UK Ltd

## Slide 3: NR AH # 2 WF R4-1706909
The CDL models and procedure for co-efficient generation are defined in 7.7.1 of 38.901 and require decision to be made on several parameters.
Key input parameters to decide are
  Carrier frequency
  NLOS or LOS
  Desired delay spread (function of scenario)
  BS Tx antenna assumption
  Channel bandwidth (to determine cluster consolidation in time domain)

## Slide 4: Issues
Scenario selection
  [5] proposes several scenarios are needed based on LOS/NLOS, ISD, delay spread
  How do scenarios map to CDL-A/B/C/D/E
Scaling for delay spread
  [1] apply desired DS to normalized CDL values
Single cluster model
  [1] proposes this although no specific justification is provided

## Slide 5: Issues
Truncation of clusters by power
  [1] proposes deleting clusters below -10 dB
  Some concerns this threshold may need to be lower, particularly with large delay spreads
Removal of cluster AsA, ZsA
  [1] proposes setting AsA and ZsA to 0 degrees to create a simplified model suitable for requirements that depend primarily on the cluster AoA (e.g. beam tracking)
  The loss of Doppler fading due to 0 angle spread is proposed to be replaced with baseband Doppler
  The equivalence of this approach for different DUT antenna types needs to be studied
Rank
  [3] proposes to define the rank, agreed to focus on 2

## Slide 6: Issues
Channel bandwidth
[4] showed the impact of time domain filtering based on channel bandwidth

## Slide 7: Issues
Angle translation and scaling
  [4] describes the process in 38.901 to translate and scale angular parameters
  No specific values are proposed
TDL models
  [4] proposes use of TDLs for some requirements

## Slide 8: Issues
  [5] discussed the need to agree a Tx antenna pattern and apply it to the CDL models. Currently there is no understanding how to apply the Tx pattern as the antenna pattern aspects I 38.901 apply to TDL models
    Proposal 5: BS antenna array is planar.
    Proposal 6: The single element BS antenna pattern is based on table 7.3-1 in 38.901.
    Proposal 7: BS antenna array model should be specified in order to simulate suitability of the test systems.
Tx antenna application

## Slide 9: Metrics for comparing
[2] proposes the following metrics for the channel models
  Capacity CDF at an SNR
  Condition number

## Slide 10: Agreements
Use 38.901 CDL table structure and methods for scaling
Use of TDLs is not precluded
Recommendations
  Move discussion on channel models into RRM/demod WI
  Channel model realizations should be test case specific

## Slide 11: Decisions to be made
  Scenarios
    NLOS/LOS, [indoor office, [street canyon] …, delay spread (ISD)
  Cluster count and AoA
    Use sources such as mmMAGIC, NYUSIM to create channel model realizations within the framework of 38.901
  Angular translation and scaling
  UE speed and direction
  TX antenna pattern
  Dynamic channel models for RRM
How to apply Tx antenna pattern to 38.901 is FFS