## Slide 1
3GPP TSG-RAN WG4 RAN4 #84
Berlin, Germany, August 21st-25th, 2017
R4-1708867
WF on upper limit for spurious emission for NR BS
Nokia, Nokia Shanghai Bell, NTT Docomo, Ericsson, Huawei

## Slide 2: Background (1)
Following agreement [1] was done during RAN4#82bis meeting:
1. Limit the upper frequency below 100 GHz in the core specification as proposed in table 1. Value is FFS, reasonable test system complexity and uncertainties need to be considered while setting the requirement.
2. BS Spurious emission for NR BS>6 GHz as proposed in Table 2:
[1] R4-1704003, “On spurious emission for NR BS”, Nokia, Alcatel-Lucent Shanghai Bell
Fundamental frequency range | Frequency range for measurements | 
 | Lower limit | Upper limit (The test should include the entire harmonic band and not be truncated at the precise upper frequency limit stated)
6 GHz-13 GHz | 30 MHz | 26 GHz
13 GHz-[FFS] GHz | 30 MHz | 2nd harmonic
Table 1: Spurious emissions frequency range for NR BS >6 GHz
Frequency range | Maximum level | Measurement Bandwidth | Note
30MHz ‑ 1GHz | -13 dBm | 100 kHz | Note 1
1 GHz – [FFS] GHz |  | 1 MHz | Note 2, Note 3
NOTE 1: Bandwidth as in ITU-R SM.329 [4] , s4.1 NOTE 2: Bandwidth as in ITU-R SM.329 [4] , s4.1. NOTE 3: Upper frequency limited by reasonable test system dynamic range |  |  | 
Table 2: BS Spurious emission limits for NR BS >6 GHz

## Slide 3: Background (2)
Upper limit for spurious emission limit was discussed during RAN4 NR#2 and RAN4#84 meetings in [1] to [3]:
[1] R4-1706782 Upper limit for the spurious region for 28GHz band Huawei, HiSilicon
[2] R4-1706845 NR BS spurious emissions Nokia, Alcatel-Lucent Shanghai Bell
[3] R4-1707654 NR BS spurious emissions for mmWave Nokia, Nokia Shanghai Bell

## Slide 4: Way forward on upper limit for spurious emission for NR BS Range 2 (1)
For TS 38.104 core specification:
- Upper limit of frequency range of spurious emission for NR Bands above 24 GHz is specified as 2nd harmonics of the upper frequency edge of the DL operating band in GHz as shown in table:
Spurious frequency range | Maximum level | Measurement Bandwidth | Note
30MHz ‑ 1GHz | -13 dBm | 100 kHz | Note 1
1 GHz – 2nd harmonic of the upper frequency edge of the DL operating band in GHz |  | 1 MHz | Note 1, Note 2
NOTE 1: Bandwidth as in ITU-R SM.329 [2] , s4.1. NOTE 2: Bandwidth as in ITU-R SM.329 [2] , s4.1. Upper frequency as in ITU-R SM.329 [2] , s2.5 table 1. |  |  | 

## Slide 5: Way forward on upper limit for spurious emission for NR BS Range 2 (2)
For TS 38.141 conformance specification:
- Upper limit of frequency range of spurious emission for NR Bands above 24 GHz is specified as 2nd harmonic of the upper frequency edge of the DL operating band, but is limited to [TBD GHz] as shown in table:
Spurious frequency range | Maximum level | Measurement Bandwidth | Note
30MHz ‑ 1GHz | -13 dBm | 100 kHz | Note 1
1 GHz – min(2nd harmonic of the upper frequency edge of the DL operating band in GHz; [TBD GHz]) |  | 1 MHz | Note 1, 2, 3
NOTE 1: Bandwidth as in ITU-R SM.329 [4] , s4.1 NOTE 2: Bandwidth as in ITU-R SM.329 [2] , s4.1. Upper frequency as in ITU-R SM.329 [2] , s2.5 table 1 NOTE 3: Upper frequency of the spurious range limited by reasonable test system dynamic range |  |  |