## Slide 1: WF on V2X Resource Selection/Reselection
Qualcomm Inc., LG Electronics, Huawei
R4-1709091
3GPP TSG-RAN WG4 Meeting #84
Berlin, Germany, 21 – 25 Aug, 2017

## Slide 2: Background
Current test setting only test lower bound for measurement error
For Resource Selection/Reselection, there are parameters that are up to UE implementation in RAN1 spec that make testing challenging:
  The set of candidate subframes is [n+T1, n+T2]. Mtotal = T2 – T1 is the number of candidates
  T1 <= 4 up to UE implementation
  20 <= T2 <= 100 up to UE implementation.
  T2 shall meets the delay requirement.
  SA is the set of candidates that have RSRP lower than TRSRP
  If SA < 0.2 * Mtotal, TRSRP increases by 3dB
  SB is ceil(0.2 * Mtotal) element in SA that has lowest RSSI.
  What can be observed is a random element of SB
  Uncertainty of T1 and T2 creates uncertainty of SA and SB for any given setting

## Slide 3: Way Forward
On Resource Selection/Reselection: Companies are encouraged to bring analysis on how to
  Reduce uncertainty of T1 and T2
  Given T1 and T2, reduce uncertainty of SA and SB
  Given uncertainty of SA and SB, how to derive the test metric.
Slide 4 & slide5 show option1
  Other options are not precluded
Test on Resource Selection/Reselection can be addressed in maintenance part.

## Slide 4: Option 1
For RSRP measurement test on Resource Selection/Reselection:
  Option1:
    Metric : Rate of PSSCH transmission on [4~20] > 99%
      Because it is always included in [n+T1, n+T2]
    Active Sidelink UE i (i=0,1,….,99)
      RSRP UE i(i=0,1,2,3, 20,21,…,99) = -79dBm/15kHz
      RSRP UE i(i=4,5,…,19) = -94dBm/15kHz
      Thr_RSRP = -84dBm/15kHz

## Slide 5: Option 1
For S-RSSI measurement test on Resource Selection/Reselection:
  Option1:
    Metric : Rate of PSSCH transmission on [4~20] > 99%
      Because it is always included in [n+T1, n+T2]
    Active Sidelink UE i (i=0,1,2,3, 20,21,...,99)
      S-RSRP UE i(i=0,1,2,3, 20,21,…,99) = -85.4dBm/15kMHz
      Noc = -95dBm/15kHz
      Thr_RSRP = infinite