## Slide 1: WF on the OTA RX requirement
CMCC
R4-1709184
Agenda :8.28.3.5
Document for: Approval
3GPP TSG RAN WG4 Meeting #84
Berlin, Germany, 21 - 25 August, 2017

## Slide 2
Way Forward
For IBB, ACS and IMD requirement:
Option 1 : Based on OTA REFSENS
Option 2 : Based on min SENS
Option 3 : Wanted based on min SENS, interferer based on OTA REFSENS
Option 4(next slider) : 1+2 ,i.e. 2 levels, one based on OTA REFSENS plus another based on min SENS
  Note. For option 4 testing can be managed by reducing the number of conformance test directions
  Example use option 1 for extremes directions and use option 2 for reference direction
Note: min SENS means lowest declared EIS in OTA sensitivity declarations (related to OSDD)
Companies submit opinions on above options next meeting

## Slide 3
Add additional IBB, ACS ,IMD OTA test based on minimum sensitivity:
OTA Wanted signal level= minimum sensitivity + 6dB ;
OTA Interference signal level= minimum sensitivity + ∆;
∆ for OTA ACS test =Conducted ACS interference level – P reference;
∆ for OTA IBB test =Conducted blocking interference level – P reference;
∆ for OTA IMD test =Conducted IMD interference level – P reference;
P reference: conducted sensitivity level
Definition of the minimum sensitivity:
Minimum sensitivity is the lowest sensitivity in all declared OSDD.
Minimum sensitivity capture the whole system performance which should include array gain, baseband combing ability and receiver units ability.
Test direction:
This OTA test is performed in the OSDD which has the minimum sensitivity.
Option1. Use the extreme directions associated with the RoAoA when the receiver target direction is at the reference direction (requires some additional conformance directions declarations).
Option2. Use the existing extreme steering directions at the extremes of the redirection range(declared OSDD)and the reference direction .
Description of Option 4

## Slide 4
[1] R4-1707839, Discussion on eAAS Receiver OTA Requirements, CMCC
[2] R4-1708116, On receiver requirements, Ericsson
[3] R4-1708499, Revisiting OTA reference sensitivity and OTA sensitivity, Nokia, Nokia Shanghai Bell
Reference