## Slide 1: Way forward for CRS-IM related advanced receiver impact analysis for network-based CRS-IM
Ericsson
3GPP TSG-RAN WG4 Meeting #84 Berlin, Germany, 21 - 25 August 2017
R4-1710178

## Slide 2: RAN4 conclusions
RAN4 has the following observations for network-based CRS mitigation impact on legacy advanced receiver:
  CRS-IC receiver
    The performance of legacy CRS-IC receiver in the network with the network-based CRS mitigation is slightly (at most 0.3 dB) worse than the performance in the legacy network for the worse case when UE is in the cell-edge.
    The performance of legacy CRS-IC receiver in the network with network-based CRS mitigation is much better than the performance in the legacy network when UE is in the cell center

## Slide 3: RAN4 conclusions
  Control channel IC
    Type A:
      The performance has negligible degradation with network-based CRS mitigation
    Type B:
      The Performance has some degradation with network-based CRS mitigation, but still significant gain are observed compared without control channel IC
  NAICs
    When NAICs signaling is not provided, there is no any performance impact