## Slide 1: 3GPP TSG-RAN WG4 Meeting #84bis Dubrovnik, Croatia, 9 – 13 October, 2017
Qualcomm Inc
MCS table for 256QAM and FD-MIMO
R4-1710434

## Slide 2: 256QAM MCS table
Existing 256QAM MCS table is sub-optimal for CFI=1 case
  In link adaptation test, using 256QAM MCS table leads to lower throughput than using 64QAM MCS table in 23~31dB CINR range

## Slide 3: 256QAM MCS table
Existing 256QAM MCS table is sub-optimal for CFI=1 case
  Performance degradation is confirmed in fixed MCS simulation
256 QAM |  |  |  |  | 64QAM |  |  |  | 
MCS | CFI | TBS | Code Rate | SPEF | MCS | CFI | TBS | Code Rate | SPEF
20 | 1 | 63,776 | 0.556 | 4.4488 | 27 | 1 | 63776 | 0.741 | 4.4488

## Slide 4: 256QAM MCS table
Existing 256QAM MCS table is sub-optimal for CFI=1 case
  RAN1 designed 256QAM CQI/MCS table for CFI=3
  If CFI=1 is used, modulation order selection is not optimal anymore

## Slide 5: FD-MIMO case
Some TBS becomes unusable in FD-MIMO scenario with large CSI-RS overheads
  64QAM MCS table, TM9, 32 CSI-RS tones, CFI=3

## Slide 6: FD-MIMO case
Some TBS becomes unusable in FD-MIMO scenario with large CSI-RS overheads
  256QAM MCS table, TM9, 32 CSI-RS tones, CFI=3

## Slide 7: FD-MIMO case
TM9 fixed MCS simulation
  Simulation assumption
    CFI = 3
    PDSCH is scheduled only in CSI-RS subframes, i.e., SF 2/7
    EVA5L channel
  MCS 8 and 9 is not usable due to too high code rate with QPSK
  MCS 15 and 16 is not usable due to too high code rate with 16QAM

## Slide 8: Solution to the problem
For 256QAM case
  Problem for CFI=1 case can be resolved by using 64QAM for MCS 20 and 21
  However, this solution would cause suboptimal modulation order selection for CFI=3 case
For FD-MIMO case
  Problem can be resolved by using 16QAM for MCS 8 and 9 and 64QAM for MCS 15 and 16
  However, for SF without CSI-RS tones, existing modulation mapping would be better
Global optimum solution seems to require using different modulation order for same TBS size depending on number of available data tones

## Slide 9: Way Forward
RAN4 acknowledges that existing MCS table for 256QAM is suboptimal
  Use of 256QAM can lead to lower PDSCH throughput than using 64QAM in some CINR range
RAN4 acknowledges that existing MCS table is suboptimal in SFs with large CSI-RS overhead in FD-MIMO deployment
  Some MCS becomes unusable in SFs with large CSI-RS overhead due to too high code rate
RAN4 sends LS to RAN1 to ask to fix the problem