## Slide 1: WF on measurement capability and measurement gap for NR
Intel
3GPP TSG-RAN WG4 RAN#84 Bis
Dubrovnik, Croatia, October 9th-13th, 2017
R4-1711275
Document for: Approval

## Slide 2: Agreement on UE capability for FR1/2 measurements
Introduce UE capability to indicate
  Independent measurement gaps can be supported for FR1 and FR2 measurement objects respectively. That includes the case the configured measurement gaps are identical for FR1 and FR2 Or
  Single measurement gap can be configured per UE
Send LS to RAN2 to introduce the related signaling

## Slide 3: Agreement on MGL
For UE supports single and per UE gap, three MGL are introduced, 6ms, [4]ms and 3ms
For UE support independent gap for FR1/2, the following MGL are introduced
  FR1 target measurement: 6ms, [4]ms and 3ms
  FR2 target measurement :
    With FR1/LTE serving cell: 6ms, [4]ms and 3ms
    With FR2 serving cell: 6ms, [4]ms, 3ms, [1+x] ms, [2+x] ms, [5+x]ms
    Note: x is defined based on RF switching time and TBD in RAN4#85
    Non-NR-capable UE does not need to support new gap other than 3ms or 6ms
Send LS to RAN2 that
  up to three MGL will be introduced UE supporting single and per UE gap
  For UE supports independent gap for FR1/2,
    Up to 3 MGL are introduced for FR1 target measurement
    Up to 3 MGL are introduced for FR2 target measurement with FR1/LTE serving cell
    Up to y MGL are introduced for FR2 target measurement with FR2 serving cell
    Note: 3≤y≤6, y will be settled in RAN4#85 once the RF switching time is decided
    Note 2 : Since LS needs to be sent in RAN4#84bis, signaling supporting y=6 can be assumed for now
  Use of [4]ms gap configured by LTE PCell needs update to gap pattern IDs supported in TS36.133

## Slide 4: Agreement on MGRP
Four MGRP to be introduced: 20ms, 40ms, 80ms and 160ms for NSA and SA NR UE
  If non-NR measurement objects are configured, 160ms MGRP should not be used
  40ms MGRP LTE requirements will apply if 20ms MGRP common gap is configured
  Use of 20ms MGRP configured by LTE PCell needs update to gap pattern IDs supported in 36.133
  For UE not supporting NR, both 20ms and 160ms should not be configured
Necessity of 20ms MGRP +6ms MGL to be confirmed by RAN4#85
Send LS to RAN2 that
  up to 4 MGRP will be introduced:20ms, 40ms, 80ms and 160ms for NSA and SA NR UE

## Slide 5: Agreement on intra-frequency measurements for FR2
Without inter-frequency or gap based mixed numerology or intra-frequency with measurement gap, UE is not expected to transmit or receive PxCCH/PxSCH on FR2 serving cells during SMTC windows for intra-frequency measurement when target SS block is within the UE active BWP.
  In this case, UE will not need gap on FR1 or LTE serving cells. This could be captured in RAN1 specs.
With inter-frequency or gap based mixed numerology or intra-frequency with measurement gap, gap is shared for all FR2 measurements

## Slide 6: Agreement on inter-frequency measurements
For FR2, gaps are needed due to RX beamforming assumption by network which is also applicable for intra-frequency measurement.
For FR1 gap usage conditions are TBD.
  if UE indicates the capability of measurement without gap, gap is not needed.
needforGaps signaling can be extended to NR+LTE NSA operation. This will be confirmed by RAN2
As RAN2 will define the gap configuration mechanism for interfrequency measurements, RAN4 can later decide on the gap usage conditions for FR1.

## Slide 7: Agreements on mixed numerology related measurements
When target SSB is within UE’s active BWP
  If UEs does not support FDM mixed numerology between SSB and non-SSB RE of serving cell, measurement gap is needed for intra-frequency measurements.
  If UE supports FDM mixed numerology between SSB and non-SSB RE, measurement gap is not needed.
  This applies to both serving and target cells
  Capability is needed.
When target SSB is within UE’s active BWP and target SSB is fully or partially overlapped with non-SSB REs of serving cell,
  If UE does not support mixed numerology between target SSB and non-SSB RE of serving cell, measurement gap is needed for intra-frequency measurements for target SSB.
  If UE supports mixed numerology between target SSB and non-SSB RE of serving cell, measurement gap is not needed for intra-frequency measurements for target SSB.
  Capability is needed.

## Slide 8: Agreements on gap sharing
Gap sharing between intra-frequency with gap and inter-frequency measurement
  Configurable by NW with up to 4 levels including equal sharing