## Slide 1: Way Forward on NR Measurement Requirements
Ericsson, […]
3GPP TSG-RAN WG4 Meeting #84bis R4-1711301
Dubrovnik, Croatia, 9th – 13th October 2017
Agenda Item: 9.7.12

## Slide 2: SS Block Based RSRP measurement requirements
Intra-frequency
  RSRP measurement period is determined based on 4 samples
    3 samples are sufficient to achieve accuracy not worse than for LTE
    1 sample may be assumed as a margin
  Measurement period = 4 * SS block periodicity, when no DRX and no measurement gaps are used by the UE, and if all SS blocks based on which the measurements are performed are actually transmitted
  FFS whether the measurement period is impacted if some SS blocks are actually not transmitted