## Slide 1: WF on UE configured Tx power for NSA DC UE at sub-6GHz
LG Electronics, InterDigital
R4-1711565
3GPP TSG-RAN WG4 #84BIS Meeting
Dubrovnik, Croatia, October 09 -13, 2017
Agenda: 9.4.3.4.3

## Slide 2: Background
LS from RAN1 for Power sharing mechanism
  For NR, UE scales down/drops NR transmission and NR power scaling details are left to UE implementation (note: it is not intended to have RAN4 test from RAN1 perspective)
    If there are two or more UL carriers, the power scaling or tx dropping can be performed for each of the UL carriers separately or jointly up to UE implementation
  For LTE, no change in power control procedure
Agreements at RAN4 at NR AH #3 meeting
  For NSA UE with both LTE band and NR band at sub-6GHz, RAN4 will follow power sharing mechanism for the configured Tx power in NSA UE RF requirements without UE capability.
In RAN4 #84BIS meeting, RAN4 discussed the Pcmax definition at sub-6GHz in the following contributions:
  R4-1710997 UE configured Tx power for NSA UE at sub-6GHz LG Electronics
  R4-1710165 Pcmax for LTE-NR DC in sub-6Ghz (FR1) InterDigital

## Slide 3: Candidate Options for LTE-NR DC UE at sub-6GHz
  Pcmax definition for LTE-NR DC UE
  Option1 : Follow Prose UE operation (R4-1710997)
    Legacy LTE Transmission is always prioritized compare to NR Transmission  LTE sub-frame is always defined as reference sub-frame to define Pcmax
  Option2 : Follow LTE DC operation while considering K1, K2 values for NR part. (R4-1710165)
    K1, K2 are currently defined in RAN1 (K1 is for HARQ feedback- PUCCH, K2 is for DCI to PUSCH timing relation)
    The NR K1,K2 flexibility is taken in account when possible for Pcmax_L, and Pcmax_H range definition for LTE-NR DC in sub-6GHz range
  Option 3 : Optimize NR DC UE Pcmax definition between options 1 and 2
  * Other solutions are not precluded.

## Slide 4
  Interested companies are invited to:
    Investigate the feasibility of the proposed options;
    Investigate other solutions if options 1,2 or 3 are considered not acceptable;
    Provide contributions and TPs on the topic for the next meeting.
Way Forward