## Slide 1: WF on NR UE REFSENS SNR
Intel Corporation, Ericsson, Huawei
3GPP TSG-RAN WG4 Meeting #84bis Dubrovnik, Croatia, 9 - 13 October 2017
Agenda Item: 9.4.4.1
R4-1711575

## Slide 2: Simulation Assumptions
Channel bandwidth and SCS
  Provide REFSENS SNR analysis for at least for the following CBW/SCS combinations
    Set 1: FR1, 10 MHz CBW + 15 kHz SCS (52 PRBs)
    Set 2: FR1, 50 MHz CBW + 30 kHz SCS (133 PRBs)
    Set 3: FR2, 50 MHz CBW + 60 kHz SCS (66 PRBs)
  Interested companies are encouraged to provide results for following combinations
    FR1
    FR2
CBW, MHz | 5 | 10 | 15 | 20 | 25 | 40 | 50 | 60 | 80 | 100
SCS (kHz) | 15 | 15 | 15 | 15 | 30 | 30 | 30 | 60 | 60 | 60
Number of PRBs | 25 | 52 | 79 | 106 | 65 | 106 | 133 | 79 | 107 | 135
CBW, MHz | 50 | 100 | 200 | 400
SCS (kHz) | 60 | 60 | 120 | 120
Number of PRBs | 66 | 132 | 132 | 264

## Slide 3: Simulation Assumptions
LDPC coding rate
  CR = 1/3
PDSCH PRB bundling:
  Option 1: No bundling
  Option 2: 2 PRB bundling
DL control channel configuration:
  3 symbols per-slot are used for DL control channel for CBW=5MHz
  2 symbols per-slot are used for DL control channel for CBW>5MHz
SS Block configuration:
  Schedule PDSCH in slots without SS blocks

## Slide 4: Simulation Assumptions
DMRS configuration:
  DMRS configuration type 1
  DMRS AP is FFS
  FFS between: Single/Double symbol DMRS
  FFS whether to configure additional DMRS symbols
PTRS configuration
  FR1: No PTRS
  FR2: PTRS is configured. KPTRS and LPTRS are FFS.
TRS and CSI-RS configuration
  Schedule PDSCH transmissions in the slots without TRS / CSI-RS.

## Slide 5: Impairments Modelling
Practical channel and noise estimation are captured in the REFSENS SNR term.
  Channel/noise estimation assumptions are for further discussion
Remaining baseband impairments
  FR1
    Remaining baseband impairments are taken into account in the IM term
    Baseband IM value is FFS
  FR2
    Remaining baseband impairments are added on top of SNR