## Slide 1: WF on the Peak EIS for n257 and n258
Sony, ...
Draft R4-1711611
3GPP TSG-RAN WG4 Meeting #84bis
Dubrovnik, Croatia, October 9-13, 2017
Agenda: 9.4.4.1.2

## Slide 2: Background
The following table is captured from chairman notes
Company | t-docs | Meetings | EIS | Remark
Huawei | R4-1707828 | 84 | -95 | SNR of -3dB is replacewith -1dB.
Intel | R4-1710431 | 84bis | -93.21 | 
LGE | R4-1710709 | 84bis | -95.9 | 
Qualcomm | R4-1711515 | 84bis | -95.9 | The original proposal of -94.9dBm was for EIS for 100MHz CBW so that it was scaled to -97.9dBm for 50MHz CBW. In addition, SNR of -3dB is replacewith -1dB and the value became -95.9dBm.
Sony | R4-1711427 | 84bis | -91 | The value of -88dBm for 100MHz CBW for UE2 was selected. The value was scaled to -91dBm for 50MHz CBW.
Agreement |  |  | -94.2 | -94.2 is the average over the five values.

## Slide 3: Way Forward
Until RAN4 #85 companies are encourage to check the REFSENS value defined as peak EIS.
Assumptions of the sensitivity equation
  The reference point for the REFSENS specification is the total power at the center of the quiet zone of the test system.
  The test signal shall be transmitted with orthogonal polarizations.
  The impact from de-sense due to practical HW implementation of the mmWave receiver + antenna array into the handset form factor
    Companies are encouraged to provide input on the value of this de-sense for the next meeting
If another reference point is decided. REFSENS value have to be adjusted