## Slide 1: Way Forward on UE EIS Spherical Coverage and Beam Correspondence
MediaTek Inc.
3GPP TSG-RAN WG4 #84bis Meeting R4-1711614
Dubrovnik, Croatia, October 9th – 13th, 2017

## Slide 2: Background (1)
mmWave UE REFSENS requirement defined at peak EIS beam direction has been tentatively agreed in last RAN4 meeting [1].
One remaining concern is whether the EIS CDF similar to EIRP CDF should also be captured to ensure receiver spatial coverage as collecting EIS CDF is a relatively time-consuming test process [2-3].
Though there were different views on the necessity of taking EIS CDF, it was generally consented that if transmit and receive beam correspondence (reciprocity) can be maintained, EIRP CDF shall also represent the EIS spherical coverage.

## Slide 3: Background (2)
In [4] in this meeting, it was proposed that beam correspondence should be guaranteed by UE design which can be indirectly verified by EIRP CDF measurement.
During online/offline discussions, companies raised the concern that beam correspondence may not exist if Tx and Rx are using separate antenna arrays.
There was also concern that beam correspondence may not be guaranteed even if Tx and Rx share the same antenna array due to design impairments.
This WF is intended to lead into the discussions on how to address EIS spherical coverage concern and EIS spec. definition.

## Slide 4: Way Forward
Companies are encouraged to study EIRP and EIS CDF correlation for several spherical coverage percentile points without and with design impairments for the following antenna array configurations
  Tx and Rx share the same antenna array.
  Tx and Rx partially share the same antenna array (for example, Rx main antenna array is shared with Tx, diversity array is not shared).
Companies are encouraged to evaluate whether EIRP CDF measurement can be a test metric to verify beam correspondence.
Companies are also encouraged to propose potential test methods other than the one based on EIRP CDF to verify EIS spherical coverage.

## Slide 5: References
[1] RAN4 NR#3 UE RF Chainman Report, Agenda 3.3.4.1.1, 3GPP TSG-RAN WG4 NR#3 AH Meeting, Nagoya, Japan, September 18th – 21st
[2] R4-1709615, “EIS requirement of mmWave UE”, Sumitomo Elec. Industries, Ltd., 3GPP TSG-RAN WG4 NR#3 AH Meeting, Nagoya, Japan, September 18th – 21st, 2017
[3] R4-1710607, “mmWave EIS requirement”, Huawei, HiSilicon, 3GPP TSG-RAN WG4 #84bis Meeting, October 9th – 13th, 2017.
[4] R4-1710897, “EIS versus EIRP spherical coverage”, MediaTek Inc., 3GPP TSG-RAN WG4 #84bis Meeting, October 9th – 13th, 2017.
[5] R4-1706067, “WF on UE Reference Architecture”, Sony, Skyworks Solutions Inc., LG Electronics