## Slide 1: WF on Single CC CH BW support for LTE Re-farming Bands
Dish, Ericsson, Nokia, Vodafone, Orange, Sprint, CMCC
3GPP TSG-RAN WG4 RAN4 #84bis
Dubrovnik, Croatia, October 9th – 13th, 2017
R4-1711733
Agenda : 9.3.1.3
Document for: Approval

## Slide 2: Background

## Slide 3: Agreed Definition of a UE CH BW
UE Channel bandwidth (R4-1709930): The RF bandwidth supporting a single NR RF carrier with the transmission bandwidth configured in the uplink or downlink of a cell. The channel bandwidth is measured in MHz and is used as a reference for transmitter and receiver RF requirements.

## Slide 4: Agreed Mandatory UE CH BWs (R4-1708845)
NR Band | Data SCS = 15kHz |  |  |  |  |  |  | Data SCS = 30kHz |  |  |  |  |  |  | Data SCS = 60kHz (for more than 1GHz bands) |  |  |  |  |  | 
 | 5MHz | 10MHz | 15MHz | 20MHz | 25MHz | [40MHz] | [50MHz] | 10MHz | 15MHz | 20MHz | 25MHz | [40MHz] | [50MHz] | [60MHz] | 10MHz (NOTE) | 15MHz | 20MHZ | 25MHz | [40MHz] | [50MHz] | [60MHz]
1.427-1.518G | Yes | Yes | Yes | Yes |  |  |  | Yes | Yes | Yes |  |  |  |  | Yes | Yes | Yes |  |  |  | 
Band 1 | Yes | Yes | Yes | Yes |  |  |  | Yes | Yes | Yes |  |  |  |  | Yes | Yes | Yes |  |  |  | 
Band 3 | Yes | Yes | Yes | Yes | Yes |  |  | Yes | Yes | Yes | Yes |  |  |  | Yes | Yes | Yes | Yes |  |  | 
Band 7 | Yes | Yes | Yes | Yes |  |  |  | Yes | Yes | Yes |  |  |  |  | Yes | Yes | Yes |  |  |  | 
Band 8 | Yes | Yes | Yes | Yes |  |  |  | Yes | Yes | Yes |  |  |  |  | NA |  |  |  |  |  | 
Band 20 | Yes | Yes | Yes | Yes |  |  |  | Yes | Yes | Yes |  |  |  |  |  |  |  |  |  |  | 
Band 28 | Yes | Yes | Yes | Yes |  |  |  | Yes | Yes | Yes |  |  |  |  |  |  |  |  |  |  | 
Band 41 |  | Yes | Yes | Yes |  | Yes | Yes | Yes | Yes | Yes |  | Yes | Yes | Yes | Yes | Yes | Yes |  | Yes | Yes | Yes
Band 66 | Yes | Yes | Yes | Yes |  | Yes |  | Yes | Yes | Yes |  | Yes |  |  | Yes | Yes | Yes |  | Yes |  | 
Band 70 | Yes | Yes | Yes | Yes | Yes |  |  | Yes | Yes | Yes | Yes |  |  |  | Yes | Yes | Yes | Yes |  |  | 
Band 71 | Yes | Yes | Yes | Yes |  |  |  | Yes | Yes | Yes |  |  |  |  | NA |  |  |  |  |  | 
NOTE: 90% spectrum utilization may not be achieved |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
UE shall meet either a single carrier or CA based RF requirements for the channel bandwidths that is equal to or smaller than UE maximum channel bandwidth for any SCS.
RAN4 should agree some threshold value for which BW’s should be supported by single CC configuration.

## Slide 5: Agreement on UE Maximum CH BW
UE maximum channel bandwidth is a UE capability. (R4-1708845)
UE shall support any Rel-15 channel bandwidth that is smaller than its UE supported maximum channel bandwidth. (R4-1706321)
The maximum channel bandwidth supported by UE can be different for UL & DL and SCS specific. (R4-1706321)
Different maximum channel bandwidths can defined for different SCS (R4-1706321)
  Maximum channel bandwidths for certain SCS can be smaller than the ones listed above but not larger
UE Maximum CH BW below 6 GHz is 100MHz (R4-1706321)

## Slide 6: Single CC CH BW support for LTE Re-farming Bands
Proposal at RAN4#84bis (R4-1711336)
  RAN4 to define a CH BW threshold of 40 MHz or 50 MHz for any LTE re-farming band, which UEs shall support by single CC configuration

## Slide 7: RAN4#84bis agreement

## Slide 8: UE single CC CH BW support for LTE re-farming bands
For each band, UE shall support all the specified CH BWs according to CH BWs in slide #4
  5, 10, 15, 20, 25, 40, 50, [60] MHz are mandatory
  [60], 80, 100 MHz are optional (Band 41)
  UE shall meet single CC requirements for these BWs
  * CH BW table to be updated in RAN4#85
Carrier Aggregation support shall be discussed separately
The minimum UE maximum CH BW shall be according to the agreed CH BWs
Low cost UE capability (i.e. low data rate devices) is not precluded and is to be handled separately