## Slide 1: WF on Channel Raster for NR
Qualcomm Incorporated, Ericsson, Nokia
3GPP TSG-RAN WG4 RAN#84 Bis
Dubrovnik, Croatia, October 9th-13th, 2017
R4-1711734
Document for: Approval

## Slide 2: Band n41 raster
Adopt SCS based raster for Band n41
Band n85(SUL band covering the same frequency range as n41) will use the channel raster defined for SUL bands which is FFS

## Slide 3: 100kHz Based Raster
Raster entries are given by the following equation for each band
  Lower band edge(MHz)+ N*0.1MHz, N chosen such that last entry is at Upper band
Raster to subcarrier position mapping
  Raster points to the center of the channel
    SC#0 of RB# NRB/2 for even number of RBs
    SC#6 of RB# floor(NRB/2)for odd number of RBs

## Slide 4: SCS Based Raster
Raster will be based on absolute frequency values
  The raster positions will be integer multiples of 15kHz for sub6 bands
  The raster positions will be integer multiples of 60kHz for mmWave range bands
Options for numbering of the raster entries:
  Raster entries are band specific
  Raster entries are indexed from 0kHz
Raster to subcarrier position mapping
  Raster points to the center of the channel
    SC#0 of RB# NRB/2 for even number of RBs
    SC#6 of RB# floor(NRB/2)for odd number of RBs

## Slide 5: RB/Subcarrier location with multiple numerologies
How the UE determines the RB placement for different numerologies is FFS