## Slide 1
3GPP TSG-RAN WG4 Meeting #85 R4-1712373
Reno, Nevada, USA, 27 November - 1 December, 2017
Agenda item: 8.22.2 UE RF [LTE_1024QAM_DL-Core]
Document for: Approval
UE capability application for DL1024QAM
KDDI Corporation

## Slide 2: Background/Proposals
In past RAN4 meetings, it had extensively discussed whether multilevel modulation features (such as DL256QAM or UL256QAM) would be supported per UE or per band (groups).
This contribution kicks off initial discussion for DL1024QAM and proposes KDDI’s position on this topic.
<KDDI’s proposal>
Our proposal is to support DL1024QAM feature per band basis (namely, NOT per UE basis).

## Slide 3: Justification
    <RAN4 history>
      DL256QAM  Supported per UE
      UL64QAM  Supported per band
      UL256QAM  Supported per band
    <Per UE support option>
      UE vendors are mandated to test all of bands. This is not cost effective because operator does not always support high order modulation in all of bands which they have. Especially for DL1024QAM, there would be quite limited points where DL1024QAM can be operated under macro cell conditions.
    <Per band support option>
      UE implementation cost can be optimized.
      One of possible concerns for this option is that DL1024QAM will not be supported in certain operators’ band(s).

## Slide 4: Conclusion
RAN4 is invited to approve below proposal.
Proposal: From UE capability perspective, DL1024 QAM should be supported per band basis (NOT per UE basis).