## Slide 1
3GPP TSG-RAN WG4 Meeting #85 R4-172373
Reno, Nevada, USA, 27 November - 1 December, 2017
Agenda item: 7.2.1 [LTE_feMTC-Core]
Document for: Approval
Way forward on B1 Cat.M2 A-MPR requirements
KDDI Corporation

## Slide 2: Background/Proposals
Way forward was approved in RAN4#84 [1]. According to [1], it was identified that possible four cases should be evaluated to protect PHS in Japan.

## Slide 3: WF: Case#1 and Case#2 (20MHz CBW)
Simulation results were input in RAN4#85 at least from one company [2]. According to it,
  Case#1: No A-MPR is required for protecting PHS.
  Case#2: A-MPR is required. One single value should be decided in this meeting because this WI is Rel. 14.

## Slide 4: WF: Case#3 and Case#4 (15MHz CBW)
Simulation results were input in RAN4#85 least from one company [2]. According to it,
  Case#3: No A-MPR is required for protecting PHS.
  Case#4: No A-MPR is required for protecting PHS.

## Slide 5: Proposals
Proposal#1: For case#1, #3 and #4, no A-MPR is required for B1 Cat.M2 UE to protect PHS in Japan.
Proposal#2: For case#2, A-MPR value should be fixed in this meeting.
Proposal#3: After approval of A-MPR value for case#4, CRs should be agreed as well. Tdoc numbers are already reserved in [3] - [4], so we ask chairman to handle them even if they will be late contributions.

## Slide 6: [draft] A-MPR table for B1 Cat.M2 UE
Network Signalling value | Requirements (subclause) | E-UTRA Band | Narrowband bandwidth | Resources Blocks (NRB) | A-MPR (dB)
NS_01 | 6.6.2.1.1 | Table 5.5-1 | 1.4, 3, 5 | Table 5.6-1 | N/A
… | … | … | … | … | …
NS_05 | 6.6.3.3.1 | 1 | 5 | [see table below] | 
NS_06 | 6.6.2.2.3 | 12, 13,14 | 1.4, 3, 5 | Table 5.6-1 | N/A
… | … | … | … | … | …
NS_35 | 6.6.2.2.7 | 71 | 1.4, 3, 5 | Table 5.6-1 | N/A
Table 6.2.4E-2: Additional Maximum Power Reduction (A-MPR) for category M2 UE
Channel Bandwidth [MHz] | Parameters |  |  |  |  |  | 
20 | Fc [MHz] | 1930 |  |  |  |  | 
 | RBstart | 0-1 | 2 – 25 | 26 - 49 | 50 - 73 | 74 – 97 | 98-99
 | NB index | N/A | #1 | #2 | #3 | #4 | N/A
 | LCRB [RBs] | ≤1 | ≤24 | ≤24 | ≤24 | ≤24 | ≤1
 | A-MPR [dB] | 0 | TBD | 0 | 0 | 0 | ≤0
Table 6.2.4E-xx: A-MPR for NS_05

## Slide 7: Reference
[1] R4-1707427, “Co-existence between B1 Cat.M2 UE and PHS in Japan”, KDDI
[2] R4-1712454, “UE category M2 A-MPR to protect PHS services”, Nokia
[3] R4-1712379, “Cat.F CR for introducing B1 Cat.M2 UE A-MPR in Japan into 36.101”, KDDI
[4] R4-1712380, “Cat.A CR for introducing B1 Cat.M2 UE A-MPR in Japan into 36.101”, KDDI