## Slide 1: MIMO OTA TRMS requirements for B5 and B19
CATR
3GPP TSG-RAN WG4 Meeting #85 R4-1712791
Reno, USA, November 27 – December 1, 2017
Agenda item: 6.2
Document for: Approval

## Slide 2: Background
The MIMO OTA requirements framework was approved in Qingdao MIMO OTA Ad-hoc [R4-1706413]:
TRMS results for band 5 have been provided in [R4-1709058, R4-1711066, R4-1707998, R4-1712789];
The performance difference between B5 and B19 is discussed in [R4-1712790];
P6: The following percentile is picked from the overall TRMS CDFs for requirements:
  -For TRMS at 70%TP: 85 percentile of the CDF for TDD bands and [85] percentile (to be bounded by 80 and 90) for FDD bands of TRMSaverage,70
  -For TRMS at 95%TP: 85 percentile of the CDF for TDD bands and [85] percentile (to be bounded by 80 and 90) for FDD bands of TRMSaverage,95

## Slide 3: B5&B19 CDF curve
As discussed in [R4-1712791], the devices have same performance at B5 and B19, so we merge the B5 and B19 results into one CDF curve. The figure below shows the CDF curve of the B5+B19 TRMS results in 3GPP RAN4 data pool.
Chart: B5+B19, CDF(58 samples)
| -98.91 | -98.766000000000005 | -97.563972174008953 | -97.106999999999999 | -96.935720000000003 | -96.47 | -96.313999999999993 | -95.975999999999999 | -95.412703740941581 | -95.246829368005507 | -94.765951251790696 | -94.652809999999988 | -94.492620000000002 | -94.347894999999994 | -94.147460000000009 | -94.060330388932215 | -93.458880000000008 | -92.866434999999996 | -92.294677166723659 | -91.651174999999995 | -88.9893
70%TP | 0 | 0.05 | 0.1 | 0.15 | 0.2 | 0.25 | 0.3 | 0.35 | 0.4 | 0.45 | 0.5 | 0.55 | 0.6 | 0.65 | 0.7 | 0.75 | 0.8 | 0.85 | 0.9 | 0.95 | 1
95%TP | 0 | 0.05 | 0.1 | 0.15 | 0.2 | 0.25 | 0.3 | 0.35 | 0.4 | 0.45 | 0.5 | 0.55 | 0.6 | 0.65 | 0.7 | 0.75 | 0.8 | 0.85 | 0.9 | 0.95 | 1

## Slide 4: Proposal for B5&B19 requirements
Following the approved framework, values (85% percentile values in the CDFs) in table below should be approved as MIMO OTA TRMS requirements for B5 and B19 in free space configuration:
Channel Model |  | SCME urban micro-cell | 
Operating band | RS-EPRE Unit | TRMS | 
 |  | Average, 70 | Average, 95
5 | dBm/15 kHz | -93 | -91
19 | dBm/15 kHz | -93 | -91

## Slide 5: Reference
R4-1706413, “Proposals on TRMS framework,” CATR, 3GPP RAN4 MIMO OTA ad-hoc, June 2017
R4-1709058, “TRMS results for harmonization and PAD devices,” CATR, 3GPP RAN4 #84, August, 2017
R4-1711066, “MIMO OTA measurement results for low band,” NTT DOCOMO, INC., SGS Wireless, 3GPP RAN4 #84bis, Oct 2017
R4-1709061, “TRMS joint band passing rate worksheet,” Intel, 3GPP RAN4 #84, August, 2017.
R4-1707998, “MIMO OTA measurement results for band 1 and 19,” NTT DOCOMO, INC., SGS Wireless, RAN4 #84, August, 2017
R4-1712789, “TRMS results for Band 5 and Band 19,” CATR, 3GPP RAN4 #85, Dec, 2017.
R4-1712790, “TRMS performance analysis for band 5 and band 19,” CATR, 3GPP RAN4 #85, Dec, 2017.