## Slide 1: Way Forward on the number of beams and cells
Ericsson
3GPP TSG-RAN WG4 Meeting #85 R4-1713760
Reno, Nevada, USA, November 27th – December 1st 2017
Agenda Item: 9.7.3.1

## Slide 2: Background
In LTE, the UE is required to be able to measure and monitor the performance of:
  8 intra-frequency cells for each intra-frequency layer
  4 inter-frequency cells for each inter-frequency layer, up to 3 inter-frequency layers or 8 inter-frequency layers (with increased carrier monitoring)
In NR, UE is required to simultaneously monitor based on SSB at least [R4-1709909]:
  Below 6 GHz
    [8] intra-frequency cells
    [4] inter-frequency cells per frequency layer
The measurement capability shall be defined per reference signal type [R4-1709909]:
  Option 1: define capability on number of cells per frequency layer and number of beams per cell
  Option 2: define capability on number of beams per frequency layer
  Option 3: define capability on number of cells per frequency layer and number of beams per frequency layer

## Slide 3: Background
Observations
  Up to 64 beams for mmwaves, most of beams are not suitable for particular UEs in practice
  Unnecessary complexity to keep track of too many beams
  Too many or even all beams from the same cell may not be the best universal solution, e.g., for mobility, high-speed UE, SON, or positioning

## Slide 4: Proposal 1
Two sets of requirements, e.g.,
  for intra-frequency at least:
    Set 1: N1 beams and 8 cells
    Set 2: N2 beams and 1 cell
  for inter-frequency at least:
    Set 1: M1 beams and 4 cells
    Set 2: M2 beams and 1 cell
UE is configured whether it shall meet Set 1 or Set 2 requirements
N1, N2, M1, M2 can be either be per carrier frequency or per cell

## Slide 5: Proposal 2
Option 1 (preferred):
  Number of beams is the number of beams per carrier frequency, e.g., for mmwaves:
    N1 = [32] beams (intra-frequncy) per carrier frequency
    N2 = N1
    M1 = [16] beams (inter-ferquency) per carrier frequency
    M2 = M1
Option 2:
  Number of beams is the number of beams per cell, e.g., for mmwaves:
    N1 = [4] beams (intra-frequncy) per carrier frequency
    N2 = [32]
    M1 = [4] beams (inter-ferquency) per carrier frequency
    M2 = [16]