## Slide 1: WF on NR UE REFSENS SNR
Ericsson
3GPP TSG-RAN WG4 Meeting #85 Reno, US, 27 Nov - 1 Dec 2017
Agenda Item: 9.4.4.1
R4-1714028

## Slide 2: Background (1/2)
The simulation assumptions were agreed as following from previous meeting.
  Channel bandwidth and SCS
    Provide REFSENS SNR analysis for at least for the following CBW/SCS combinations
      Set 1: FR1, 10 MHz CBW + 15 kHz SCS (52 PRBs)
      Set 2: FR1, 50 MHz CBW + 30 kHz SCS (133 PRBs)
      Set 3: FR2, 50 MHz CBW + 60 kHz SCS (66 PRBs)
    Interested companies are encouraged to provide results for following combinations
      FR1
      FR2
CBW, MHz | 5 | 10 | 15 | 20 | 25 | 40 | 50 | 60 | 80 | 100
SCS (kHz) | 15 | 15 | 15 | 15 | 30 | 30 | 30 | 60 | 60 | 60
Number of PRBs | 25 | 52 | 79 | 106 | 65 | 106 | 133 | 79 | 107 | 135
CBW, MHz | 50 | 100 | 200 | 400
SCS (kHz) | 60 | 60 | 120 | 120
Number of PRBs | 66 | 132 | 132 | 264

## Slide 3: Background (2/2)
Following the previous slides as agreed simulation assumption
  DL control channel configuration:
    3 symbols per-slot are used for DL control channel for CBW=5MHz
    2 symbols per-slot are used for DL control channel for CBW>5MHz
  SS Block configuration:
    Schedule PDSCH in slots without SS blocks
  TRS and CSI-RS configuration
    Schedule PDSCH transmissions in the slots without TRS / CSI-RS.
  Practical channel and noise estimation are captured in the REFSENS SNR term.

## Slide 4: Online agreements made in RAN4#85
The following agreements were made and captured in the chairman’s notes.
  Use CR=1/3 for the REFSENS SNR simulation assumption.
  Use PRB bundling size 2 for the REFSENS SNR simulation assumption.
  Still use -1dB SNR value for the NR UE REFSENS analysis target
  Agree on the following REFSENS definition procedure
    Use tentative SNR = -1 dB as the assumption for NR RF REFSENS definition
    Define REFSENS FRC and define corresponding SNR value (SNRFinal) as per RAN1 work progress (final SNR value may be different from tentative SNR)
    Replace the tentative SNR value with final SNR value once it is finalized as follows: REFSENSFinal = REFSENS + SNRFinal – SNR

## Slide 5: WF for further simulation assumptions
Take the following configuration as the working assumption unless further issues are identified.
  DMRS configuration:
    Option 1: Front loaded Type 1, DL-DMRS-len = 1, DL-DMRS-add-pos = 2
    Option 2: Front loaded Type 1, DL-DMRS-len = 1, DL-DMRS-add-pos = 3
    Option 3: Front loaded Type 1, DL-DMRS-len = 1, DL-DMRS-add-pos = 1
  PTRS configuration
    FR1: No PTRS
    FR2:
      Option 1: No PTRS
      Option 2: PTRS is configured
        KPTRS = 2 (transmitted in every 2nd RB)
        LPTRS = 1 (transmitted in each OFDM symbol)
  Other options are not precluded in case issues are identified by companies.
Both ideal and practical channel estimations results are to be provided for alignment purposes.
  Keep previous agreement: Practical channel and noise estimation are captured in the REFSENS SNR term.

## Slide 6: WF for IM
Companies are encouraged to bring more input in next meeting for components contributing to IM.
FR1
  Remaining impairments are taken into account in the IM term
FR2
  Remaining impairments are added on top of SNR.