## Slide 1: WF on receiver sensitivity requirements for FR2
Nokia, Nokia Shanghai Bell
3GPP TSG-RAN WG4 Meeting #85 Reno, Nevada, USA, 27 November – 1 December 2017
Agenda Item: 9.5.3.1.2
R4-1714145

## Slide 2: Background
Contributions on BS receiver sensitivity requirements for FR2 have been discussed in RAN4#85:
  [1] R4-1712614 TP to TS 38.108 - OTA sensitivity (10.2) Huawei
  [2] R4-1712620 Discussion on minimum FR2 Rx sensitivity and min antenna gain Huawei
  [3] R4-1712689 Proposals on mmWave NR BS Receiver Antenna Gain Nokia, Nokia Shanghai Bell
  [4] R4-1713023 Array antenna receiver characteristics Ericsson
  [5] R4-1713065 Discussion on OTA receiver minimum antenna gain for FR2 NR BS NTT DOCOMO, INC.
  [6] R4-1713285 Considerations on OTA sensitivity for FR2 Ericsson
  [7] R4-1713286 TP to TS 38.104: FR2 REFSENS Ericsson
  [8] R4-1713445 On mm-wave radome and performance impact Ericsson

## Slide 3: Way forward
Reference sensitivity power level, PREFSENS [dBm] = [X] - ΔOTAREFSENS
[X] = -174 + 10*log(BW) + NF + SNR + IM
  BW is the transmission bandwidth configuration of the wanted signal in Hz
  NF is the noise figure of the BS (include allowed receiver desensitization for MR and LA BS)
  SNR is the required SNR to achieve 95% of maximum throughput (obtain from simulation)
  IM is implementation margin
ΔOTAREFSENS
  Declared by BS manufacturer in [1]dB step within the range [10] to [30]dB
  Reflect BS implementation parameters like antenna array gain