## Slide 1: Way forward on CRS muting for UE demodulation
Ericsson
3GPP TSG-RAN WG4 Meeting #85
Reno, NV, USA, 27 November – 1 December, 2017
R4-1714247

## Slide 2: Background
RAN1 are going to introduce a capability signaling to mute CRS outside the BL UE narrowband/wideband, and have sent LS [R4-1704502] to RAN4 to ask the
  Minimum amount(s) of CRS
  Value(s) of X corresponding to number of PRBs outside the narrowband/wideband used by BL UEs for CRS.
Idea of the CRS muting in Rel-15 eFeMTC WI is to introduce a capability to make sure that BL UE uses the signal transmitted only within the UE maximum channel width.
If the eNB knows the BL UE has this capability then eNB can turn off the CRS transmission on RPBs which is not used by BL UEs. Therefore, RAN1 is asking the amount(s) of CRS the network can turn off.

## Slide 3: Example of CRS muting for UE demodulation
Example of CRS transmission
  X=2 PRBs outside the narrowband used for PDSCH transmission
  Y=1 subframe before the MPDCCH/PDSCH transmission (warm-up)
  Y=1 subframe after the MPDCCH/PDSCH transmission (cool-down).

## Slide 4: Agreements for UE demodulation
RAN4 agreed with the necessary amounts of CRS for BL UEs as follows:
  Frequency domain
    X=1 for Cat-M1 (1.4MHz channel bandwidth)
    X=0 for Cat-M2 (5MHz channel bandwidth)
  Time domain
    Cool-down
      Y=1 for CRS-based PDSCH transmission at the end of last narrowband transmission (both CEModeA and CEModeB)
      Y=0 for other cases
    Warm-up
      Y=1 before target MPDCCH and PDSCH narrowband (both CEModeA and CEModeB)
      Y=0 for other cases