## Slide 1: WF on channel raster
Nokia,
R4-1714294

## Slide 2: Background
Previous Way-forwards
R4-1706323 WF on Channel Raster and Synchronization Raster/SCS for sub 6GHz, Huawei, Ericsson, Nokia, Qualcomm
R4-1706981 WF on RF channel raster for sub6GHz and mmWave bands, Qualcomm
R4-1709934 WF on DL Channel Raster for NR, Qualcomm, Ericsson
R4-1711734 WF on Channel Raster for NR, Qualcomm, Ericsson, Nokia
Contributions in RAN4#85
R4-1712765 NR channel raster, ZTE
R4-1713260 NR absolute radio frequency channel number, ZTE
R4-1712331 On NR channel raster, Intel
R4-1712712 NR RF channel raster, Ericsson
R4-1713779 Discussion on frequency numbering scheme, Nokia
R4-1712939 Discussion on NR ARFCN, Huawei
R4-1712182 Channel Raster for Suplemental UL and UL sharing, Qualcomm
R4-1712940 Channel raster for UL subcarrier alignment, Huawei
R4-1713262 Further consideration on PRB placement, ZTE
R4-1713263 Channel raster to subcarrier mapping, ZTE

## Slide 3: Background
R4-1712182, “Channel Raster for Suplemental UL and UL sharing”, is agreed for SUL bands.

## Slide 4: Discussion points
Whether if the raster points at
  channel centre / carrier frequency (subcarrier mapping as agreed in RAN4#84bis)
  reference to the PRB grid placement
Whether if the raster is
  Band specific
  Global (for FR1(100kHz raster), FR1(15kHz raster) and/or FR2)
Frequency numbering options
  Absolute offset from 0Hz
  Relative offset from the band edge
  Relative offset from the sync raster
Granularity (step size) of offset
  The same as channel raster
  Finer than the channel raster
Frequency range to be covered
  Up to at least [86/120] GHz
How to distinguish overlapping bands
How to distinguish uplink and downlink

## Slide 5: Agreement (1)
NR-ARFCN defines the absolute radio frequency
  it is globally defined.
    frequency band and duplex (uplink or downlink) are not distinguished.
It is RAN2 to decide how to signal the frequency of Pcell, Scell, SUL, and/or the reference frequency for PRB grid, etc, using NR-ARFCN or other means.

## Slide 6: Agreement (2)
NR-ARFCN for FR1
  Option A1: Define two global sets from 0Hz to 6GHz
    the integer multiple of 15kHz
    the integer multiple of 100kHz
  Option B1: Define one global set from 0Hz to 24GHz
    the integer multiple of 5kHz from 0 to 3GHz
    the integer multiple of 15kHz from 3 to 24GHz
  Option C1: Define offset from sync raster
    Sync raster + float sync + PRB offset

## Slide 7: Agreement (3)
NR-ARFCN for FR2
  Option A2: Define one global set from 24 GHz to 100 GHz
    the integer multiple of 60kHz
  Option B2: Define offset from sync raster
    Sync raster + float sync + PRB offset

## Slide 8: Agreement (4)
NR-ARFCN range for each frequency band is tabulated in RAN4 specs.
Corresponding signaling is for RAN2 to design.

## Slide 9: Working assumption of frequency numbering
FREF = FREF-Offs + ΔFGlobal (NREF – NREF-Offs)
Frequency range | Range covered | ΔFGlobal | FREF-Offs | NREF-Offs | Range of NREF
FR1 | 0 – 3000 MHz | 5 kHz | 0 MHz | 0 | 0 – 599999
FR1 | 3000 – 24000 MHz | 15 kHz | 3000 MHz | 600000 | 600000 – 1999999
FR2 | 24000 – 100000 MHz | 60 kHz | 24000 MHz | 2000000 | 2000000 – 3266667