## Slide 1: Way Forward on NR CA Bandwidth Class Definition
MediaTek Inc., Nokia, Ericsson
3GPP TSG-RAN WG4 #85 Meeting R4-1714366
Reno, Nevada, USA, Nov. 27th – Dec. 1st, 2017

## Slide 2: Background (1)
CA bandwidth class was originally introduced in E-UTRA technical specifications to distinguish UE capability in supporting contiguous carrier aggregation (CCA).
In RAN4 NR AH #3 meeting, it was agreed that CA bandwidth class would be introduced to NR [1].
In RAN4 #84bis meeting, it was further agreed that [2],
  CA bandwidth class shall be with aggregated channel bandwidth and number of contiguous CC(s)
  NR CA BW class A shall be defined with one CC
Based on the above agreement, several proposals were brought up in this meeting [3-6], as summarized in the last slides.

## Slide 3: Concerns to be Addressed for NR CCA (1) What is the CA acronym for?
  Is CA acronym used to describe NW deployment or UE receiver configuration?
  Same acronym cannot be used for both because acronym could be different for NW deployments and UE receiver configuration for same CA configuration
  Operators have used CA acronym to describe their NW deployments
  Different UEs have different implementations thus different acronyms would be needed for same NW deployment. In LTE CA configurations of class C is used for at least two different UE architectures (single and dual receiver) and UE architecture is implementation issue.

## Slide 4: Concerns to be Addressed for NR CCA (2)
How to address forward compatibility if new wider CBW is introduced in future releases?
How to avoid the explosion of bandwidth combinations?
  Impact to signaling complexity
  Impact to specifications complexity

## Slide 5: Agreements
Agreements
  BW class C is agreed to be 2 CC
  CA acronym is used at least for NW deployments
  RAN4 to hold off NR CCA proposals till CA bandwidth class is clearly defined.

## Slide 6: Way Forward
Companies to study whether a separate CCA acronym is needed from UE side to address different UE architecture.
  From signaling point of view
  From UE RF requirements point of view
  Other possible signaling solutions to address the topic
How to define BW Class for Contiguous Intra-band DC
Study if only one CA bandwidth class table for both new NR bands and LTE re-farmed bands is sufficient.

## Slide 7: Background (2) – Proposals for FR1

## Slide 8: Background (2) – Proposals for FR2

## Slide 9: References
[1] R4-1710083, “WF on BCS and CA bandwidth class for LTE-NR DC”, Nokia, Nokia Shanghai Bell, 3GPP TSG-RAN WG4 NR#3 AH Meeting, September 18th – 21st, 2017
[2] R4-1711973, “Consideration on NR CA bandwidth class”, Huawei, Hisilicon, 3GPP TSG-RAN WG4 Meeting #84bis, October 9th – 13th, 2017
[3] R4-1712419, “NR CA bandwidth classes”, Ericsson, Qualcomm, AT&T, Telstra, Verizon, 3GPP TSG-RAN WG4 #85 Meeting, Nov. 27th – Dec. 1st, 2017.
[4] R4-1712930, “Way forward on NR CA bandwidth class definition”, MediaTek Inc., 3GPP TSG-RAN WG4 #85 Meeting, Nov. 27th – Dec. 1st, 2017.
[5] R4-1712966, “Further consideration on NR CA bandwidth class”, Huawei, Hisilicon, 3GPP TSG-RAN WG4 #85 Meeting, Nov. 27th – Dec. 1st, 2017.
[6] R4-1713001, “Further considerations on NR CA bandwidth class”, ZTE Corporation, 3GPP TSG-RAN WG4 #85 Meeting, Nov. 27th – Dec. 1st, 2017.