## Slide 1: WF on pi/2 BPSK spectrum shaping and power class in FR2
Intel Corporation, Apple, Qualcomm, IITH, LGE, Nokia , Huawei, Motorola Mobility
R4-1714373
3GPP TSG-RAN WG4 Meeting #85
Reno, Nevada, USA, November 27 – December 1, 2017
Agenda: 9.4.3.1.2

## Slide 2: Background
RAN4 has discussed the pi/2 BPSK pulse shaping filter and the power class requirement definition for FR2
  Slides #4 – 5 summarize the proposed peak EIRP values
Views on the challenges associated with UE design were exchanged
Views on the impact on network design were exchanged
Views on the selection of a reference waveform for peak EIRP definition were exchanged

## Slide 3: Agreements on Pi/2 BPSK Spectrum Shaping for FR2
The spectrum shaping filter and associated requirements are applicable only to FR2
  UE shall be allowed to employ spectral shaping for pi/2 BPSK
  We propose the following X1, X2 and Y values, as defined in R4-1711569, for spectrum flatness requirement so as to not preclude any of the proposed filters
    [X1 = 6dB, X2 = 20 dB, Y = -15 dB]
    [X3 such that X2 = X1 + X3]
    Impact on network performance should be studied
PA Output Power for FR2: Qualcomm and IITH have shown that the PA can be driven with BPSK at a higher power level than with QPSK while meeting the requirements
  The waveform defined by BW = 100MHz, SCS=60KHz, DFT-S-OFDM QPSK, 128RB0 is the reference waveform with 0dB MPR and is used for the power class definition
  MPR requirements for waveforms that operate at higher output power than the reference waveform can be defined with a negative value
  The Pcmax requirement includes an additional term to account for negative MPR in both Pcmax_L and Pcmax_H terms

## Slide 4: Summary of proposed peak EIRP values @ 28GHz
Parameter | Unit | Intel | LGE | MediaTek | Huawei | Samsung | Motorola | Qualcomm plastic | Qualcomm glass
# ant elements |  | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4
Avg. element gain (per polarization) | dBi | 4.00 | 5.00 | 4.50 | 4.0 | 4.50 | 2.50 | 5 | 5
Antenna roll-off loss vs frequency | dB | -2.00 | -1.00 | -3.00 | -1.00 | -1.00 | -0.50 | -2.3 | -2.3
Realized ant. array gain | dBi | 8.00 | 10.00 | 7.50 | 9.00 | 9.50 | 8.00 | 8.72 | 8.72
Polarization gain | dB | 2.80 | 2.50 | 2.50 | 2.00 | 2.50 | 2.80 | 2.80 | 2.80
Total implementation loss (nominal) | dB | -6.75 | -7.25 | -5.10 | -4.85 | -6.75 | -4.25 |  | 
Total implementation loss (worst-case) | dB | -9.60 | -10.00 | -7.45 | -8.70 | -9.60 | -6.10 | -3.3 | -4.3
PA operating point (nominal) | dBm | 14.00 | 14.00 | 14.00 | 14.00 | 14.00 | 14.00 |  | 
PA operating point (minimum) | dBm | 14.00 | 14.00 | 14.00 | 14.00 | 14.00 | 14.00 | 12.0 | 12.0
Peak EIRP (nominal) | dBm | 24.05 | 25.25 | 24.90 | 26.15 | 25.25 | 26.55 |  | 
Tolerance | dB | 3.85 | 3.75 | 3.85 | 3.85 | 2.85 | 2.85 |  | 
Peak EIRP (minimum) | dBm | 20.20 | 21.50 | 21.05 | 22.30 | 22.40 | 23.70 | 26.24 | 25.24
NOTE 1: PA operating point defined for the DFT-s-OFDM full allocation waveform with the QPSK modulation

## Slide 5: Summary of proposed peak EIRP values @ 39GHz
Parameter | Unit | Intel | LGE | MediaTek | Huawei | Samsung | Motorola | Qualcomm plastic | Qualcomm glass
# ant elements |  | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4
Avg. element gain (per polarization) | dBi | 4.00 | 4.0 | 4.50 | 4.50 | 4.50 | 1.50 | 5 | 5
Antenna roll-off loss vs frequency | dB | -2.50 | -1.50 | -1.50 | -1.00 | -1.50 | -0.50 | -0.6 | -0.6
Realized ant. array gain | dBi | 7.50 | 8.5 0 | 9.00 | 9.50 | 9.00 | 7.00 | 10.42 | 10.42
Polarization gain | dB | 2.80 | 2.50 | 2.50 | 2.00 | 2.80 | 2.80 | 2.80 | 2.80
Total implementation loss (nominal) | dB | -7.95 | -8.50 | -6.10 | -5.85 | -7.75 | -4.25 |  | 
Total implementation loss (worst-case) | dB | -10.90 | -11.45 | -8.55 | -8.80 | -10.20 | -6.70 | -5.0 | -6.3
PA operating point (nominal) | dBm | 14.00 | 14.00 | 12.50 | 12.00 | 12.50 | 14.00 |  | 
PA operating point (minimum) | dBm | 14.00 | 14.00 | 12.50 | 12.00 | 12.50 | 14.00 | 10.5 | 10.5
Peak EIRP (nominal) | dBm | 22.35 | 22.5 | 23.90 | 23.65 | 24.05 | 25.55 |  | 
Tolerance | dB | 3.95 | 3.95 | 3.45 | 3.95 | 3.45 | 3.45 |  | 
Peak EIRP (minimum) | dBm | 18.40 | 18.55 | 20.45 | 19.70 | 20.60 | 22.10 | 24.74 | 23.44
NOTE 1: PA operating point defined for the DFT-s-OFDM full allocation waveform with the QPSK modulation

## Slide 6: Agreements on peak EIRP
The handheld UE peak EIRP range is defined as follows and will be captured in TS38.101-2 in this meeting
  For 28 GHz: [21.2-25.2] dBm
  For 39 GHz: [19.4-23.7] dBm
Companies are encouraged to provide additional analysis with the intention to finalize the UE peak EIRP requirement

## Slide 7
References
TDoc | Title | Source
R4-1712931 | TP for UE RF TR 38.817-01: mmWave power class | Sumitomo Elec. Industries, Ltd
R4-1712934 | TP for UE RF TR 38.817-01: mmWave EIRP spherical coverage requirement | Sumitomo Elec. Industries, Ltd
R4-1712319 | UE power class for FR2 | Intel Corporation, Apple, OPPO, Samsung, LGE, Xiaomi, MediaTek, Motorola, Huawei
R4-1712320 | TP on UE power class for FR2 | Intel Corporation
R4-1712386 | mmW Power class | Qualcomm Incorporated
R4-1712525 | TP to 38.101-2: Maximum output power | Ericsson
R4-1712923 | mmWave peak EIRP evaluation result update | Huawei, HiSilicon
R4-1713193 | Further evaluation on NR UE power class at mmWave | LG Electronics France
R4-1713849 | Network performance impact of practical peak EIRP | Apple (UK) Limited, Intel Corporation