## Slide 1: Way forward on SSB-based inter-frequency measurement requirements
Huawei, HiSilicon, …
3GPP TSG-RAN WG4 Meeting #86 Athens, Greece, 26th February – 2nd March, 2018
Agenda item: 7.9.4.2
R4-1802593

## Slide 2: Background
We have reached the following agreements for SSB-based intra-frequency measurement requirements in RAN4 #AH1801:
  For FR1, it is proposed to set TPSS/SSS_sync, T SSB_measurement_period and TSSB_time_index requirement as:
    TPSS/SSS_sync = max( 600, [5 or 6] x SMTC_period ) ms (1)
    TSSB_time_index = max( [TBD], [2+X] x SMTC_period ) ms (2)
    TSSB_measurement_period = max( 200, [5] x SMTC_period ) ms (3)
  For FR2, requirements of TPSS/SSS_sync, T SSB_measurement_period and TSSB_time_index are given as:
    TPSS/SSS_sync = max( [X1], [Y1] x N1 x SMTC_period ) ms (4)
    TSSB_time_index = max( [X2], [3+Y2] x N2 x SMTC_period ) ms (5)
    TSSB_measurement_period = max( [X3], [Y3] x N3 x SMTC_period ) ms (6)
SSB-based inter-frequency measurement requirements need to be defined with the consideration of gap sharing impacts.

## Slide 3: Way forward
This way forward is to capture agreements on inter-frequency measurement requirement methodologies
  Introduce for gap sharing impact
  should be defined by scaling with gap sharing schemes
  For FR1, it is proposed to set TPSS/SSS_sync, T SSB_measurement_period and TSSB_time_index requirement as:
    TPSS/SSS_sync = Max(TBD, [6]x max(MRGP, SMTC period)x Kinter) (1)
    TSSB_time_index = Max(TBD, [2+2]x max(MRGP, SMTC period)x Kinter) (2)
    TSSB_measurement_period = Max(TBD, [5]x max(MRGP, SMTC period)x Kinter) (3)

## Slide 4: Way forward
  For FR2, it is proposed to set TPSS/SSS_sync, T SSB_measurement_period and TSSB_time_index requirement as:
    TPSS/SSS_sync = Max(TBD, [6]x max(MRGP, SMTC period) x N1 x Kinter) (1)
    TSSB_time_index = Max(TBD, [3+3]x max(MRGP, SMTC period) x N2 x Kinter) (2)
    TSSB_measurement_period = Max(TBD, [5]x max(MRGP, SMTC period) x N3 x Kinter) (3)
  For FR2, reuse the TBD values in the equations from FR1