## Slide 1: Way forward on SSB-based inter-frequency measurement requirements
Huawei, HiSilicon, MediaTek, [Ericsson], Nokia, Nokia Shanghai Bell
3GPP TSG-RAN WG4 Meeting #86 Athens, Greece, 26th February – 2nd March, 2018
Agenda item: 7.9.4.2
R4-1802593

## Slide 2: Way forward
Measurement objects with same SMTC periodicity and offset within the same FR range should share the same delay requirement and the same measurement gap pattern.
Strive to address the SMTC overlapping issue should be based on SMTC configuration grouping and each group has its own scaling factor

## Slide 3: Way forward
A per-carrier scaling scheme is suggested for defining inter-frequency measurement requirements within the same gap pattern. Assuming that there are totally Nfreq inter-frequency layers to be monitored via this gap pattern, the requirement of inter-frequency carrier #i can be expressed as:
      Tinter, carrier_i = M×MAX(SMTCcarrier_i, MGRP) × Nscaling,carrier_i , i=1,2…Nfreq.
  M stands for the required sample number for inter-frequency measurement.
    Companies are encouraged to provide views on the impact of AGC issue on the M value
  Nscaling,carrier_i is the scaling factor of carrier #i and Nscaling,carrier_i ≤ Nfreq
  When all SMTC are non colliding (no measurement gap contains SMTC from more than one frequency layer) then Nscaling,carrier_i =1, for i=1,2…Nfreq
  Companies are encouraged to suggest the principle to decide the value of Nscaling,carrier_i
    For any inter-frequency carrier #i and inter-frequency carrier #j,
      If SMTC periodicity and offset of these two inter-frequency carriers are the same, then Nscaling,carrier_i = Nscaling,carrier_j
    The value of Nscaling,carrier_i is suggested to consider the number and SMTC periodicity and offset of carriers whose SMTC occasions are fully or partially colliding with the SMTC occasions of carrier #i.
  Note1: Above requirement does not yet consider the delay caused by gap sharing with intra-frequency measurement and DRX mode.
  Note2: The value of Nscaling,carrier_i is suggested to consider the number of interRAT carriers configured in the UE