## Slide 1: Way Forward on inter-RAT measurements for RRC_CONNECTED in 38.133
Ericsson, …
3GPP TSG-RAN WG4 Meeting #86 R4-1803480
Athens, Greece, 26th Feb – 2nd March, 2018
Agenda Item: 7.9.10.2

## Slide 2: Proposals for inter-RAT NR – E-UTRAN measurements
The measurements include: RSRP, RSRQ, and RS-SINR
The requirements are specified for SA only
The inter-RAT requirements are based on LTE inter-frequency requirements
  Without DRX: TIdentify = TBasic, Identify *480/TInter1 * Nfreq, SA
    TBasic, Identify = 480 ms
    Nfreq, SA is defined in Section 9.1.3.3
    TInter1 is the minimum available time for gap-based measurements during TBasic, Identify
  With DRX (up to 10.24 s DRX cycle): as in 36.133 but based on Nfreq, SA
The requirements are applicable:
  without an explicit E-UTRAN neighbour cell list containing physical layer cell identities
  for UE configured with an appropriate measurement gap pattern according to Table 9.1.2-3
Separate sections for:
  NR – E-UTRAN FDD measurements (9.4.2)
  NR – E-UTRAN TDD measurements (9.4.3)